## Slide 1: Communication methods

## Slide 2: Learning objectives
Define serial and parallel transmission methods
Discuss the advantages and disadvantages of serial and parallel transmission
Define and compare synchronous and asynchronous data transmission
Describe the purpose of start and stop bits in asynchronous data transmission

## Slide 3: Data communication
Data communication is the transmission of data form one device to another
  Between computers and other devices such as printers on a network
  Between components along a bus within a computer such as between RAM and the processor
The data transferred are encoded according the medium of transmission
  In wired methods this can be by electrical signals in copper cables or light in fibre optic
  In wireless methods data are transmitted as radio waves

## Slide 4: Serial transmission
Serial transmission refers to transmission of one bit of data at a time between computer components
Only a single wire is used
Serial transmission down a wire is sent as a change in electrical voltage
Voltages change between high voltage (5v) and low voltage (0v) to encode 1 and 0 respectively
The voltages are put on a single wire and sent to another computer that can read these voltages and convert back into binary digital data
Example: USB (Universal Serial Bus) peripheral devices
Sender
Receiver
0 1 0 0 0 1 1 0

## Slide 5: Serial Transmission

## Slide 6: Serial transmission
0 Volts
5 Volts
0
1
0
1
1
0

## Slide 7: Parallel transmission
Parallel data transmission means that several bits of data are sent at the same time along multiple wires between computer components
We can normally send 8 bits, 16 bits, 32 bits and 64 bits at the same time
Parallel transmission is normally used to transmit data between internal computer components
Sender
Receiver
1
0
0
0
0
0
1
1

## Slide 8: Parallel Transmission

## Slide 9: Serial versus Parallel transmission
 | Advantages | Disadvantages
Serial | It can be used over longer distances than parallel transmission | It is a slow method of data transfer
Parallel | It is quicker than serial data transfer | Skew- Over longer distances bits can get skewed. This results in the bits going out of synchronisation and arriving at different times and therefore out of order. Crosstalk - Interference between wires, so the data can become corrupted.

## Slide 10: Skew
Sender
Receiver
1 0 0 0
0 1 0 1
0 1 1 1
0 0 0 0
0 1 1 0
0 1 0 1
1 1 1 1
1 0 0 1

## Slide 11: Parallel Transmission with skew

## Slide 12: Synchronous transmission
The signals are sent at regular intervals in a continuous stream
Timing signals are also sent allowing the sending and receiving clocks to be synchronised
The sender needs to transmit the data at the same rate that the receiver reads the data
Synchronous transmission and parallel transmission are normally used together

## Slide 13: Synchronous transmission
Read signal 0 1 0 0 1 1 0
0 Volts
5 Volts
Read signal 0 1 0 1 1 0
0 Volts
5 Volts
Transmission 0 1 0 1 1 0
signal
Receiver clock speed too fast
Same receiver and sender clock speed

## Slide 14: Asynchronous transmission
In asynchronous data transmission the data are sent in chunks (packets) normally as one byte or ACSII character
The transmission contains a start and stop bit that specify the beginning and end of the sequence and a parity bit for error checking
The start bits are used to prepare the receiver to start receiving data
The stop bit resets its state allowing it to read the next sequence
The values of the start bit and stop bit must be different. ie if the start bit is 0 then the stop bit is 1 and vice versa
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0
Stop bit
Start bit
Parity bit
Data
Direction of data transmission

## Slide 15: Asynchronous transmission
Start and stop bits are needed so we can delineate when out character end and another starts.
Idle bits are transmitted when no characters are being transmitted.
When a start bit is received the fixed length character follows with the parity bit.
Sender
Receiver
0 1 0 0 0 1 1 0 1 1 1 1 0 1 1 0 1 0 1 0 0 1 1 1 1 1 1 1 1
Idle/stop bits
7-bit character
Start bit
Parity bit
Idle/
stop bits
Start bit
7-bit character

## Slide 16: Asynchronous versus synchronous transmissions
Synchronous transmission requires a clock to allow synchronisation between the sender and receiver. Data are sent continuously
Asynchronous transmission is slower than synchronous transmission, because more data are sent
We need to send extra bits owing to the need for parity, stop and start bits
In synchronous transmission data are sent continuously but in asynchronous transmission data are sent in packets

## Slide 17: Question: Asynchronous transmission
The following sequence of data has been transmitted using asynchronous transmission. The idle/stop bit is 1, the start bit 0 and even parity has been used. Each character is 7 bits corresponding to an ASCII character. What is the word that is transmitted? The right most bits are transmitted first so the word will appear backwards.
111110110010101111101100101011110111001001111010100011111
Direction of data transmission

## Slide 18: Answer: Asynchronous transmission
The following sequence of data has been transmitted using asynchronous transmission. The idle/stop bit is 1, the start bit 0 and even parity has been used. Each character is 7 bits corresponding to an ASCII character. What is the word that is transmitted? The right most bits are transmitted first so the word will appear backwards.
11111 0 1100101 0 11111 0 1100101 0 1111 0 1110010 0 11 1 1010100 0 11111
eerT = Tree

## Slide 19: Plenary
Explain the difference between serial and parallel transmission?
What are the benefits of serial transmission over parallel transmission?
What is the difference between synchronous and asynchronous data transmission?
What are the purpose of start and stop bits in data transmission?
The following data are transmitted using asynchronous transmission using even parity. What are the start, stop and parity bits?
 |  | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 
Stop bit | Parity bit | Data |  |  |  |  |  |  | Start bit
Direction of data transmission