## Slide 1: Input & Output

## Slide 2: Learning objectives
Describe the principles of operation of the following devices:
  Barcode reader
  Digital camera
  Laser printer
  RFID
Discuss the different context in which the different input devices are used

## Slide 3: Bar code scanner
The bar code scanner emits laser light and detects reflected light off the bar code.
Laser light can be emitted at red wavelengths (which is visible) or infrared (which is not) depending on the scanner.
The columns of the bar code which are coloured black and white are evenly spaced and have the same width and correspond to a bit.
The white columns reflect the laser light and this corresponds to a 0.
The black columns do not reflect back the reflected light and this is encoded as a 1.
Parity error checking allows the scanner to determine which way round the scanner has read the bar code.
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1

## Slide 4: QR codes
QR (Quick Response) codes are a type of barcode that normally direct users to a website.
Digital cameras on phones can be used to scan QR codes
What is QR Code - YouTube

## Slide 5: RFID (Radio Frequency Identification)
RFID can uniquely identify an object.
RFID is a wireless systems that operates at radio frequencies and is composed of tags and readers
Passive RFID chips do not have their own power source which allows for them to be small.
The RFID chips get their power source from nearby radio transmitters (or RFID detectors) that are constantly emitting radio waves.
When an RFID chip comes within range of an RFID detector, the chip is powered by the radio waves which activates the chip to transmit a signal to the detector that uniquely identifies the chip.
Active RFID has its own power source which means that it can transmit over longer distances.
What is RFID and How Does it Work? - YouTube

## Slide 6: Digital camera
The purpose of a digital camera is to convert light into a digital signal which is encoded as binary.
light is focuses through a lens that is controlled by a shutter
This shutter is open for only a tiny fraction of a second and lets in the light
The light is focused onto a charged couple device (CCD).
This is an array of tiny light detectors that measures the intensity of light.

## Slide 7: Digital camera
Each detector has a filter that only allows only photons at red, green and blue wavelengths to pass.
There are twice as many cells with green filters because our eyes are more sensitive to green than the other colours.
The intensity of light (number of photons) is then converted to an electrical signal that is then encoded into binary values for each colour.
This occurs across all detectors in the CCD array and so a complete picture can be captured.
The greater the number of detectors that greater the detail that can be captured.
How do digital cameras work? | James May Q&A | Head Squeeze - YouTube
CCD Array

## Slide 8: Comparison of input devices
 | Advantage | Disadvantage
Bar code reader | Very cheap | Bar code could be obscured Bar code scanner needs to be close to object
RFID | Read fast No line-of-sight issues Can reuse tags | Needs to be close to object (for passive case) RFID dead spots
Digital camera | Clearly identify object | Need clear line of site High data storage requirements Needs to be target at object so will needs lots of cameras OCR or face recognition needed, but still not perfect

## Slide 9: Exercise
Can you think of situations where a barcodes scanner, RFID and digital cameras are used in your day to day lives?
For each of those situations explain why that input device has been used. (what are the benefits and limitations of that approach?)
Explain how you think the technology and systems might develop in the future.

## Slide 10: Bar code scanner – super-market shopping
Benefits
All products already have bar codes, and cheap to produce
Supermarkets can employ fewer people on checkouts.
Supermarkets can track exactly what people buy and collect data on each customer.
Limitations
It is easier to shoplift
Scanners can get lost and broken
Takes longer for customers to complete their shopping.
Future
Can customers use their own mobile phones cameras instead of scanners?
Could bar codes be replaced by RFID, so that whole trolly of shopping could be scanned at once?

## Slide 11: QR code quick access to website
Benefits
Do not need to type in long URL.
Limitations
People may not have their mobile phone with them
QR codes be unsightly, especially when placed on slick publicity material

## Slide 12: RFID – Student sign in system
Benefits
Nearly all students and employees in big organisations issued with ID cards that can easily accommodate an RFID chip
Quick means of sign in
Limitations
Students (and staff too!) may forget their ID cards
Future
Use biometric data, like facial recognition or finger prints

## Slide 13: RFID taking out library books
Benefits
Several books can be scanned simultaneously.
Previously books had bar codes and needed to be scanned individually which was more time consuming
Limitations
Each book needs an RFID tag
Need sensors on entry and exit, which can sometimes be triggered inadvertently

## Slide 14: RFID – Tracking runners during a race
Benefits
Do not need line-of-sight for each runner
RFID tags can be reused as they are tied to runners’ shoe-laces
Has quick read so can read thousands of runners in a short time.
Scanner can be put on the floor.
Limitations
Runner may not return tags

## Slide 15: Camera – Sign in
Benefits
Use facial recognition technology to allow sign-in to a mobile device, means that users do not need to remember a password.
Limitations
Currently not completely reliable, eg can use photo of user to access.
Concerns around racial bias. Works better for some ethnicities than others.
Should we be concerned about the collection of our biometric data by large tech companies?

## Slide 16: Camera - CCTV
Benefits
Can identify individuals
Can be used as evidence in court
Limitations
CCTV could drive crime to areas where there is no CCTV
Future
Should we be concerned about the state use of CCTV by authorities especially around issues of facial recognition? What does this mean for liberal democracies?

## Slide 17: Laser printer
At the core of the laser printer is a drum that turns and rubs against an electrically charged roller.
As it rotates the drum gets completely covered in negatively charged electrons
As the drum turns it gets hit by a laser beam, areas on the drum that are exposed to the laser beam become neutrally charged to create the image or text.
The toner which is negatively charged in the hopper is put onto another roller.
The toner is attracted to the neutrally changed areas and repelled by the negatively charged areas on the drum.
The toner is then transferred from the drum onto the positively charged paper.
Finally the paper passes through a heated roller to dry the ink.
How do printers work? (Color Laser Printer & inkjet printer) - YouTube

## Slide 18: Plenary
Go to www.padlet.com
Choose one of the devices below and describe its principle of operations
  Barcode reader
  Digital camera
  Laser printer
  RFID
Read the responses of others. What have you missed?