## Slide 1: Starter
Without looking at your notes:
List the Logic gates
Write down the truth table for each gate
Draw the symbol

## Slide 2: Boolean Circuits

## Slide 3: Learning objectives
Create and interpret truth tables for logic circuits
Show how logic circuits relate to Boolean expressions

## Slide 4: Combining logic gates
Logic gates can be combined to produce other logic gates.
For instance AND and NOT gates can be combined to produce a NAND gate.
OR and NOT gates can be combined to create NOR gates
Logic gates can be combined to create more complex logic circuits

## Slide 5: Exercise
Complete the questions in computer-systems-Boolean.docx
You may wish to use an online simulator to help:
https://academo.org/demos/logic-gate-simulator/
https://logic.ly/demo/

## Slide 6: Exercise
Complete the questions in boolean-task.docx

## Slide 7: Q1 complete the logic table for the circuit below and write the Boolean expression
A | B | E | C | D
0 | 0 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 
E

## Slide 8: Q1 complete the logic table for the circuit below and write the Boolean expression (Answer)
A | B | E | C | D
0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 1 | 0 | 0 | 1
E
E=NOT A
C= E AND B
D= NOT C
D = NOT (E AND B) Substitute in C
D = NOT((NOT A) AND B) Substitute in E

## Slide 9: Q2 complete the logic table for the circuit below and write the Boolean expression
A | B | C | D | E
0 | 0 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 

## Slide 10: Q2 complete the logic table for the circuit below and write the Boolean expression (Answer)
A | B | C | D | E
0 | 0 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
C = A AND B
D = NOT B
E= C OR B
E = (A AND B) OR (NOT B)

## Slide 11: Q3 complete the logic table for the circuit below and write the Boolean expression
A | B | C | D | E | F
0 | 0 | 1 |  |  | 
0 | 1 | 1 |  |  | 
0 | 0 | 0 |  |  | 
0 | 1 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 1 | 0 |  |  | 

## Slide 12: Q3 complete the logic table for the circuit below and write the Boolean expression (Answer)
A | B | C | D | E | F
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1
E = A AND B
D= NOT C
F = E OR D
F = (A AND B) OR (NOT C)

## Slide 13: Q4 complete the logic table for the circuit below and write the Boolean expression
A | B | C | D | E | F
0 | 0 | 1 |  |  | 
0 | 1 | 1 |  |  | 
0 | 0 | 0 |  |  | 
0 | 1 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 1 | 0 |  |  | 

## Slide 14: Q4 complete the logic table for the circuit below and write the Boolean expression (Answer)
A | B | C | D | E | F
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 0
D = A AND B
E = NOT D
F = E OR C
F = NOT(A AND B) OR C

## Slide 15: Q5 complete the logic table for the circuit below and write the Boolean expression
A | B | C | D | E
0 | 0 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 

## Slide 16: Q5 complete the logic table for the circuit below and write the Boolean expression (Answer)
A | B | C | D | E
0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0
F = NOT((A OR B) OR B)

## Slide 17: Create a Boolean expression from the truth table with 2 inputs
There is a general approach to converting a truth table into a logic circuit.
The output expressed as a Boolean expression is shown in the truth tables for a two-input expression
Where the input is a 0 the output is expressed as NOT.
We AND the two inputs
Input A | Input B | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Input A | Input B | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 18: Create a Boolean expression from the truth table with 3 inputs
Input A | Input B | Input C | Output
0 | 0 | 0 | .
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | .
1 | 0 | 1 | .C
1 | 1 | 0 | .
1 | 1 | 1 | 
Input A | Input B | Input C | Output
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
The output expressed as a Boolean expression is shown in the truth tables for a three-input expression

## Slide 19: Create a Boolean expression from the truth table with 4 inputs
Input A | Input B | Input C | Input D | Output
0 | 0 | 0 | 0 | ..
0 | 0 | 1 | 0 | .
0 | 1 | 0 | 0 | .
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | ..
1 | 0 | 1 | 0 | .C.
1 | 1 | 0 | 0 | ..
1 | 1 | 1 | 0 | .
0 | 0 | 0 | 1 | ..D
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | 
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 1 | .
1 | 0 | 1 | 1 | .C.D
1 | 1 | 0 | 1 | .
1 | 1 | 1 | 1 | 
Input A | Input B | Input C | Input D | Output
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 0 | 
1 | 1 | 1 | 0 | 
0 | 0 | 0 | 1 | 
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | 
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 1 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 
The output expressed as a Boolean expression is shown in the truth tables for a three-input expression

## Slide 20: Worked Example1: Create a Boolean expression from the Truth Table
Find the Boolean expression for the following truth table. It does not need to be simplified.
We consider only the lines with an output of 1:
We then combine each statement with an OR:
Input A | Input B | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Input A | Input B | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Input A | Input B | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 21: Worked Example2: Create a Boolean expression from the truth table
Find the Boolean expression for the following truth table. It does not need to be simplified.
We consider only the lines with an output of 1:
We then combine each statement with an OR:
A | B | C | Output
0 | 0 | 0 | .
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | C
1 | 0 | 0 | .
1 | 0 | 1 | .C
1 | 1 | 0 | .
1 | 1 | 1 | 
A | B | C | Output
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
A | B | C | Output
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 22: Create the Boolean algebra expressions from the Truth Tables
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
(NOT A AND B) OR (A AND NOT B)
(NOT A AND NOT B) OR (A AND B)
A AND NOT B
(NOT A AND NOT B AND NOT C) OR (A AND B AND NOT C)
A | B | Q
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
A | B | C | Q
0 | 0 | 1 | 0
0 | 1 | 1 | 0
0 | 0 | 0 | 1
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 1
a) b) c) d)

## Slide 23: Create the Boolean algebra expressions from the Truth Table
e)
Input A | Input B | Input C | Input D | Output
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
.

## Slide 24: Simple versus complex circuits
Different circuits can produce the same logic that given the same inputs will have the same outputs. It is always better to choose a logic circuit with fewer gates because it:
reduces production costs
reduces the heat produced
reduces energy requirement
increases speed of the circuit

## Slide 25: Plenary
Complete the diagnostic questions
boolean-logic-diagnostic-questions.pptx
Available in www.diagnosticquestions.com
Search: Boolean Logic GCSE
Link: Quiz | Diagnostic Questions

## Slide 26: Homework: Represent the following expressions as logic circuits
Complete task: circuit-task.docx