## Slide 1: Communication Basics

## Slide 2: Learning objectives
Explain broadband and dial-up internet access
Explain how bit rate and bandwidth are related.
Define the following terms:
  baud rate
  bit rate
  bandwidth
  latency
  protocol
Explain the difference between baud rate and bit rate.

## Slide 3: Telephone network – Dial up
The telephone network is (increasingly was) made of copper wires to the telephone exchange.
The telephone network uses an analogue signal where the voltage changes with time and can take on any value.
When using dial-up to connect to the internet a modem is used to convert the digital signal to an analogue signal that can be carried along the telephone line to a receiving modem that then converts the signal back from an analogue signal to digital signal.
Dial up is slow with maximum speeds of 56 Kb per second
Cannot make phone call at the same time
Sender computer
Modem converts to analogue signal
Sends over copper telephone wire
ISP Modem convers back from analogue signal to digital
ISP Server
Internet

## Slide 4: ADSL
Broadband ADSL (asymmetric digital subscriber line) also uses the same copper telephone wires but operates at higher frequency
ADSL provides much higher speed internet access than dial-up modem
A filter is used to split the signal allowing access to the telephone and internet at the same time.
The telephone operates on low frequencies at range of lower frequencies from 0 to 4 KHz.

## Slide 5: ADSL
Computer
Telephone
Filter
Internet
Copper Cable

## Slide 6: ADSL
More bandwidth is dedicated to downloading data than uploading because this meets the requirements for most users.
The differing bandwidth between for uploading and downloading is the reason why the broadband is asymmetric.
Broadband is split into narrow channels.
Typically we have 256 4KkHz channels for ADSL broadband for both upstream and downsteam.

## Slide 7: Bandwidth
Bandwidth refers to the range of frequencies at which the data can be transmitted and relates the volume of data that can be transmitted along the medium in a given time.
Expressed in hertz as the difference between the lowest and highest frequency.
There is a directly proportional relationship between bandwidth and bit rate.
That is the greater the bandwidth the greater the bit rate, because we can have a greater number of channels.

## Slide 8: Baud rate
Baud rate is the number of changes of signal per second (frequency) and is measured in Hertz.
Another way to think of it the number of symbols that you can transmit per second

## Slide 9: Bit rate
Bit rate is the number of bits transmitted per second.
The baud rate is not the same thing as with the bit rate.
More than one bit can be represented per baud
Bit_rate = baud_rate x number_of_bits_per_baud

## Slide 10
1 bit per baud
2 bits per baud
3 bits per baud
4 bits per baud

## Slide 11: Bit rate
The baud rate will be the same as the bit rate only when one bit is sent for each change of signal. In this situation there are 2 voltage levels (symbols) representing zero and one.
Voltage Level
1
0
1
1
0
Time

## Slide 12: Difference between bit rate and baud rate
Voltage Level
01
10
11
00
11
00
01
10
00
Time
It is possible to send more that 1 bit per signal change For instance if there are 4 voltage levels, the voltages can be encoded as 00, 01, 10, 11.
One signal change encodes 2 bits. In this case bit rate is twice the baud rate

## Slide 13: Latency
Latency is the delay in data transfer from one component to another. At the most fundamental level the speed of data transfer is limited by the speed of light.
Latency is also caused by transmission in the medium itself, and other necessary processing.

## Slide 14: Handshaking Protocol
A protocol is a set of rules that allow different devices to communicate with one another.
The handshaking protocol is used to establish a connection between a computer and a printer for instance.
  The sending device checks whether the receiving device is present
  The sending device asks the receiving device whether it is ready to receive data.
  The receiver responds stating whether or not it is ready
  If it is ready the data are then sent to the receiver and the receiver signals that it is busy to other devices if they contact it
  The sender transmits a stop bit to inform the receiver that all the data have been sent.
  The receiver is ready to receive further data

## Slide 15: Plenary
Explain how the hand shaking protocol works?
Define latency
Explain the difference between the bit rate and the baud rate?
What is bandwidth?
What is the relationship between bit rate and bandwidth?