## Slide 1: Fetch Decode Execute Cycle and Interrupts

## Slide 2: Learning objectives
Explain the difference between RISC and CISC chips
Explain processing pipelining
Explain processing on GPUs
Explain how the processor works
Explain the fetch, decode, execute cycle
Explain what an interrupt is

## Slide 3: RISC (Reduced instruction set chips)
RISC chips have a set of instructions that take fewer CPU cycles to execute.
RISC chips contain simple instructions.
These chips have simpler logic circuits, have fewer transistors
Each instruction that can be executed in a single CPU cycle.
It takes more operations to perform more complex instructions.
On a RISC chip complex instructions can be achieved by combining a sequence of these simpler operations.
Although RISC chips may process each operation quicker, more complex tasks will require more operations.
RISC chips can now be found in most devices including mobile phones and computers.
Complex translation required from high level programming language to the low level assembler instructions.

## Slide 4: CISC (Complex Instruction Set Chips)
The hardware architecture of the chip is more complex than for RISC chips.
More logic circuitry is needed to perform the operations.
Instructions can consist of several operations.
Instructions will take multiple clock cycles to execute.
It does mean that programs are shorter reducing requirements on memory.
More straightforward translation between high level language the assembly language.

## Slide 5: Processor pipelining
Processor pipelining allows instructions to be carried out in parallel on a single processor, thereby improving processor throughput.
The processor steps are broken down into stages, in this case fetch decode and execute stages. In reality there are more stages, but we only include these three here for simplicity
Without pipelining the stages will occur in series. The complete fetch-decode-execute cycle of the preceding operation needs to be completed before the next instruction is fetched.
Once the fetch part of the cycle has been completed in pipeline 1, it moves onto the decode part. At the same time the next instruction is fetched. When these second steps have been completed, pipeline moves onto the execute step, pipeline moves onto the decode and Pipeline 3 fetches the instruction. This process repeats itself.
Time | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
No Pipelining | Fetch | Decode | Execute | Fetch | Decode | Execute | Fetch | Decode | Execute
Pipeline 1 | Fetch | Decode | Execute |  |  |  |  |  | 
Pipeline 2 |  | Fetch | Decode | Execute |  |  |  |  | 
Pipeline 3 |  |  | Fetch | Decode | Execute |  |  |  | 

## Slide 6: Multicore and parallel processing
Parallel and multicore processing systems allow instructions and data to be processed at the same.
All processors have threads which allows processing to be performed at the same time.
Muticore processing refers to threading instructions on multiple cores on a single CPU chip.
Parallel processing refers to multiple processors as in the case of a supercomputer, processing data and instructions at the same time cross multiple CPUs.

## Slide 7: Discrete Graphics Card
You can add these graphic cards to the motherboard’s expansion slots
Graphics cards control the output to the monitor
They allow the quality of the graphics to be improved
Graphics cards have their own processing capability called a GPU (graphics processing unit), taking some of the burden away from the CPU.
These are specialised CPUs designed for graphics rendering
Graphics cards also have their own RAM
Graphics cards are connected to the monitor via ports (eg HDMI or VGA)

## Slide 8: Uses of GPUs
GPUs process data in parallel giving them a high processing throughput.
GPUs are good for tasks that are processing intensive but at the same time are highly parallelizable.
GPUs are that makes them good for:
Machine learning – Processing huge volumes of data for creating models
Video rendering
Gaming
Blockchain and cryptocurrency mining – solving complex mathematical problems to validate new transactions that are added to the blockchain.

## Slide 9: Components of a CPU
Arithmetic logic unit – The arithmetic and logic operations take place here.
Control unit – Decodes the instruction, splits it into the opcode and operand and identifies the specific operation.
Clock – The purpose is to keep all the processor components synchronised. The clock controls the processor so that it can process the instructions one-by-one and in the correct order.
Registers – Memory locations on the CPU. Much faster than cache and RAM however also much smaller. Used to store frequently accessed data and instructions. There are two types of registers general purpose and registers dedicated to a specific purpose.

## Slide 10: Processor schematic
ALU
Control Unit
Address bus
Data bus
Address | Content
Main memory
Processor
Registers
Clock
PC
MAR
MBR
CIR
ACC

## Slide 11: Dedicated registers
Memory Address Register (MAR) – The address in main memory that we wish to fetch the instruction from
Memory Buffer Register (MBR) – Holds the instruction that has been fetched from memory
Current instruction register (CIR) – Holds the contents of MBR, which is the instruction to be processed
Program Counter (PC) – This holds the memory address of the location to fetch the next instruction from.
Status Register (SR) – Gives information on such things as overflow/underflow, interrupts, parity. The status register allows an instruction to depend the outcome of the previous instruction.
Accumulator – Holds the results of arithmetic and logic computations

## Slide 12: Fetch-decode-execute cycle
The instructions are loaded into memory
The processor fetches the instruction from the main memory
The instruction is decoded so the CPU knows what to do with the instruction
The processor then executes the instruction
The result of the instruction can be stored in memory
The next instruction is then fetched from main memory and the cycle repeats itself

## Slide 13: Fetch-decode-execute
1. MAR  [PC]
2. MBR  [Memory]MAR_address
PC  [PC] +1
3. CIR  [MBR]
4. Decode [CIR]
5. Execute [CIR]
Transfer the contents of the PC to the MAR
The contents at that address is transferred back to the MBR along the data bus
At the same time the PC is incremented by one to get ready for the next cycle.
Transfer the contents of the MBR to the CIR ready to be decoded.
Control unit decodes instruction held in CIR into operand and opcode
Instruction executed by ALU for instance and result stored in Accumulator. Status register updated

## Slide 14: Fetch
Register | Content
PC | 0
MAR | 
MBR | 
CIR | 
Address | Content
0 | 00101001
1 | 11101010
2 | 11100101
3 | 10101110
Main memory
Processor

## Slide 15: Fetch: MAR  [PC]
Register | Content
PC | 0
MAR | 0
MBR | 
CIR | 
Address | Content
0 | 00101001
1 | 11101010
2 | 11100101
3 | 10101110
Main memory
Processor
Transfer the contents of the PC to the MAR
The address in MAR is transferred to main memory along the address bus
Address bus

## Slide 16: Fetch: MBR  [Memory]MAR_address ; PC  [PC] +1
Register | Content
PC | 1
MAR | 0
MBR | 00101001
CIR | 
Address | Content
0 | 00101001
1 | 11101010
2 | 11100101
3 | 10101110
Main memory
Processor
The contents at that address is transferred back to the MBR along the data bus
At the same time the PC is incremented by one to get ready for the next cycle. This can be done because the two steps do not rely on one another.
Address bus
Data bus

## Slide 17: Fetch: CIR  [MBR]
Register | Content
PC | 1
MAR | 0
MBR | 00101001
CIR | 00101001
Address | Content
0 | 00101001
1 | 11101010
2 | 11100101
3 | 10101110
Main memory
Processor
Transfer the contents of the MBR to the CIR ready to be decoded.
This allows the MBR to be used to store the next instruction during the decode and execution stages.
Address bus
Data bus

## Slide 18: Decode: [CIR]
The control unit decodes the instruction held by the current instruction register.
The instruction is divided into the opcode and the operand
ALU
Control Unit
Processor
Registers
Clock
PC
MAR
MBR
CIR
ACC

## Slide 19: Execute: [CIR]
The instruction is executed in the arithmetic logic unit.
The result is stored in the accumulator register
The status register is updated
ALU
Control Unit
Processor
Registers
Clock
PC
MAR
MBR
CIR
ACC

## Slide 21: Fetch Decode Execute Animation

## Slide 22: FDE images Slide-by-Slide

## Slide 23: Multitasking
Multitasking allows concurrent processing of multiple programs.
Instructions can only be processed one at a time on a single processing core.
Multitasking works by interleaving operations between multiple programs.
Multitasking interrupts a program so that another program can use the processor.

## Slide 24: What is an interrupt?
Interrupts are messages from software applications or hardware that request processing resources from the processor.
If the processor is performing operations already then those processes can be interrupted and suspended, and the CPU processes the interrupt request
An interrupt service routine will be executed depending on the type of interrupts.
When an interrupt occurs, the data and instruction in the registers from the interrupted job are stored in the stack so that the job can be restored after the interrupt has been dealt with.
Once the interrupt has been completed the processor resumes the job it was currently processing from where it left off. It is able to do this because the instructions and data are loaded back into registers and memory from the stack.

## Slide 25: Examples of interrupts
Hardware commands
  Computer reset
Software
  Error detection
  Overflow error
Timer
Input/output
  Pressing a key on a keyboard
  Moving the mouse

## Slide 26: Interrupt Service Routine
Stack
When an interrupt is encountered the contents of the program counter are copied to the stack and address of the instruction of the interrupt service routine is copied to the program counter.
Once all the instructions of the interrupt service routine have been executed the address in the stack is copied back into the program counter and the original processing task resumes.
Step 1
Program Counter:
0100
Interrupt service Routine address: 0111
Stack
0100
Step 2
Program Counter:
0111
Stack
Step 3
Program Counter:
0100

## Slide 27: Interrupt in the fetch execute cycle
Start
Fetch next instruction
Execute instruction
Interrupt?
Process interrupt
No
Yes
Decode instruction

## Slide 28: Architecture
dq-architecture-19.docx

## Slide 29: Homwork Past papers
AQA A level 2009 P2 June Q7
AQA A level 2010 P2 Jan Q3
AQA A level 2010 P2 June Q7
AQA A level 2012 P2 Jan Q3
AQA A level 2012 P2 Jan Q5
AQA A level 2015 P2 Jan Q1
AQA A level 2017 P2 Jan Q1
AQA AS level Specimen P2 Q6