## Slide 1: Revision: Expand the following brackets
(x + 1) (x + 3)
(a + 4) (a – 2)
(A + 2) (A + 2)
(A + B) (A + B)

## Slide 2: Revision: Expand the following brackets (answers)
(x + 1) (x + 3) x2+4x+4
(a + 4) (a – 2) a2+2a-8
(A + 2) (A + 2) A2 + 4A + 4
(A + B) (A + B) A2+B2+2AB or A.A+B.B+A.B+A.B

## Slide 3: Revision: Factorise the following expressions
x + 2x
2x + 4
3x + 6xy
A+AB
A+A+AB

## Slide 4: Revision: Factorise the following expressions (answers)
x + 2x x(1+2)
2x + 4 2(x + 2)
3x + 6xy 3x(1+2y)
A+AB A(1+B)
A+A+AB A(1+1+B)

## Slide 5: Boolean Algebra

## Slide 6: Learning objectives
Know a range of Boolean identities to simplify Boolean expressions
Apply the Boolean Laws to simplify Boolean expressions

## Slide 8: Boolean Identities
Commutative Law:
Inverse Law
AND Law
OR Law
Associative Law
Distributive Law
Other Identities

## Slide 9: Commutative Law

## Slide 10: Inverse Law
A double NOT counsels itself out

## Slide 11: AND Law
0.0=0
0.1=0
1.0=0
1.1=1
A and NOT A always opposite so if A=1, then NOT A is 0 and vice versa. For the output of an AND gate to be 1 both inputs need to be 1, but since this is not possible the output will always be 0.
Both inputs are A and are always the same, so we have either 0.0=0 or 1.1=1. Therefore the output will always take on the value of the input.

## Slide 12: AND Law
0.0=0
0.1=0
1.0=0
1.1=1
For the output of an AND gate to be 1 both inputs need to be 1, but since one of the inputs will always be 0 then the output will always be 0.
One of the inputs will always be 1 so we have 1.0=0 or 1.1=1, thus the value of the output will be the same as the input.

## Slide 13: OR Law
0+0=0
0+1=1
1+0=1
1+1=1
For an OR gate only 1 input needs to be 1 for the output to be 1. Given that we will have 1 the output will always be 1 regardless of the value of A
In this scenario we have 0+0=0 or 0+1=1. Therefore the output is the depends only on the input A.

## Slide 14: OR Law
0+0=0
0+1=1
1+0=1
1+1=1
=1
=0
In this scenario we have 1+1=1 or 0+0=0. Therefore the output is the depends only on the input A.
A and NOT A always opposite so if A=1, then NOT A is 0 and vice versa. We will always therefore have 1 as an input regardless of the value of A and this is enough for the output of an OR gate to be 1.

## Slide 15: Associative Law
This means that it does not matter the order in which the AND operators are applied:
(1 * 2) * 3 = 1 * (2 * 3)
This means that it does not matter the order in which the OR operators are applied:
(1 + 2) + 3 = 1 + (2 + 3)

## Slide 16: Distributive Law

## Slide 17: More Boolean Identities
Proof:
Proof:

## Slide 18: Order of Operation for Boolean Algebra
Order of operation
  Brackets
  NOT
  AND
  OR
  XOR

## Slide 20: Worked Example 1 - Simplify the Boolean expression
There is often more than 1 way to simplify a Boolean expression.
We will look at 2 methods to solve this expression
Method 1
Factorise
0. Apply AND law
0. Apply OR law
Apply AND law
Method 2
Multiply out brackets
0 Apply AND law
0 Apply AND law
Apply law

## Slide 21: Worked Example 2: Simplify the following Boolean expression:
Expand the brackets

## Slide 22: Worked example 3: Simplify the following Boolean expression

## Slide 23: Exercise Simplify the following Boolean expressions

## Slide 24: Exercise Simplify the following Boolean expressions: Answers
1

## Slide 25: Simplify the following Boolean expressions
.

## Slide 26: Simplify the following Boolean expressions: Answers
1
.

## Slide 27: Plenary