## Slide 1: Network Topology and network types

## Slide 2: Learning objectives
Explain and compare different network topologies
Explain and differentiate physical star and logical bus network topologies and how they work
Explain client-server networking
Explain peer-to-peer networking

## Slide 3: Bus network topology
All devices including clients, servers, printers and so on are connected to a cable called a bus. All communication is via the shared bus. At either ends of the bus is a terminator. The terminator absorbs the signal so that it is to not reflected back down the cable.

## Slide 4: Bus Network (animation)

## Slide 5: Bus Collisions

## Slide 6: Bus collisions

## Slide 7: Bus topology
Advantages
Easy and cheap to install and does not require much cable.
Easy to add more computers
Disadvantages
If the main cable fails then then the whole network fails.
Less secure as data are broadcast to all devices on the network.
Can be slow as there are collisions between data along the shared bus. Will get slower as more computers are added.

## Slide 8: Star network topology
For a star topology all devices including clients, servers, printers and so on are connected to a central hub or switch. All communication is via the hub.

## Slide 9: Star Network

## Slide 10: Star topology
Advantages
Greater security as data are only sent to the intended recipient
If any of the connections fail only a single node will be affected. The rest of the network will work as normal
Fewer collisions between data packets
Disadvantages
If the central hub fails then every computer on the network is affected
Expensive as extra cable and hardware (hubs) are needed

## Slide 11: Logical bus network topology
It is possible that a network that has been physically set up with cables based on one topology can behave as if is has been set up as another topology.
For instance, a network that has physically been set up at a star topology can behave as a logical bus network.
In this situation the hub is set up so that communication received from one computer is relayed to all the other devices on the network.

## Slide 12: Logical bus network

## Slide 13: Full Mesh Topology
In a full mesh network all devices are connected to every device allowing for direct two-way communication between the nodes

## Slide 14: Full Mesh Topology

## Slide 15: Partial Mesh Topology
In a partial mesh network not all devices are directly connected to one another. For two nodes that are not directly connected to one another they have rely on nodes in between to retransmit the packets

## Slide 16: Partial Mesh Topology

## Slide 17: Mesh topology
Advantages
There is a lot of redundancy built into the network, because if one connection fails, there are a lot of other viable routes to transmit the messages
Lower latency as message can be sent directly between computers
Disadvantages
Not very practical to set up because even a small network with a few nodes will require lots of connections: (n*(n-1))/2 connections where n is the number of nodes
Expensive to set up as a lot of cabling is needed

## Slide 18: Ring Topology
Each node is connected to two other nodes forming a ring.
When a message is sent from one device to another, the receiving devices determines whether it is the intended recipient and if not retransmits the message onto the next device.

## Slide 19: Ring Topology

## Slide 20: Ring topology
Advantages
Relatively inexpensive to set up
Can perform better than bus topology because there are fewer collisions
Disadvantages
If one node fails the whole network fails
Latency increases when sending messages from one node to another when there are a lot of nodes between the computers

## Slide 21: Network Types

## Slide 22: Client server network
In a client server network clients are connected to a server which is a central computer that provides services to the clients. These services can include:
  Providing web pages (web server)
  Providing files (file server)
  Access to email (email server)
  Database access (database server)
  Printing (print server)

## Slide 23: Client server model
Server: runs programs to serve applications to other computers
Client: a computer that makes use of a service
A client will make a request to a server. The server will run processes that are continuously listening for communications on a specific port.
When the server receives the request it then responds to the request
Hosting refers to storing of the service on the internet. For instance, in the context of the web, the host refers to the server where the website is stored and that host is publicly accessible.

## Slide 24: Client-server architecture
The client requests a service or resource from the server
The server is continuously waiting/listening for a request
The server responds to the request and waits the next request
Hub
Client
Client
Client
Client
Server
Client
Client

## Slide 25: Peer-to-peer network architecture
In a peer-to-peer network all computers can communicate directly with one another.
All computers act as both a server and client at the same time.
This allows the resources on the each of the computers to be shared with the other computers.
Each device will store its own files/resources
The files can be accessed by all other devices on the network and shared around the network
There is no server and all computers have equal status.
This is a cheap network to set up because an expensive server is not needed.
It is also possible that each computer can host different parts of a large file such as a film. This reduces the demand on a single computer.
Client
Client
Client
Client
Client

## Slide 26: Peer-to-peer file sharing
Each computer on the network will have different files. These files can then be shared with other peers.
It is also possible that each computer can host different parts of a large file such as a film. This reduces the demand on a single computer.
Find out about Napster. What happened? Why?

## Slide 27: Plenary
Go back to the model of networks that you created at the start of the lesson.
Change the network to be either a ring, bus, mesh or star
Explain to your neighbours what the advantages of your network is
Explain the difference between star and bus network topology and discuss their advantages and disadvantages