## Slide 1: Assembly Language
Alternatively use: dq-assembly-language-12.pptx

## Slide 2: What value is stored in memory location 8 once the assembly code below has been executed?
A)
3
C)
2
D)
-2
B)
5
MOV R0, #3
SUB R0, R0, #5
STR R0, 8

## Slide 3: What value is stored in memory address 24 once the assembly code below has been executed?
LDR R0, 16
LDR R1, 20
ADD R0, R0, R1
STR R0, 24
A)
1
C)
4
D)
7
B)
3
Memory address | Value
16 | 4
20 | 3
24 | 

## Slide 4: What value is stored in memory address 16 once the assembly code below has been executed?
MOV R0, #5
LSL R1, R0, #2
STR R1, 16
A)
0
C)
5
D)
20
B)
2

## Slide 5: What value is stored in memory address 12 once the assembly code below has been executed?
MOV R0, #5
LSR R1, R0, #2
STR R1, 12
A)
1
C)
5
D)
10
B)
2

## Slide 6: What binary value is stored in memory address 12 once the assembly code below has been executed?
MOV R0, #4
AND R1, R0, #2
STR R1, 12
A)
0000
C)
1010
D)
1111
B)
1000

## Slide 7: What binary value is stored in memory address 12 once the assembly code below has been executed?
MOV R0, #4
ORR R1, R0, #2
STR R1, 12
A)
1010
C)
0110
D)
0000
B)
1110

## Slide 8: What inary value is stored in memory address 12 once the assembly code below has been executed?
MOV R0, #7
EOR R1, R0, #2
STR R1, 12
A)
1010
C)
1100
D)
0000
B)
1110

## Slide 9: What value is stored in memory address 12 once the assembly code below has been executed?
MOV R0, #8
MVN R1, R0
STR R1, 12
A)
0001
C)
0111
D)
1010
B)
1000

## Slide 10: What value is stored in memory address 48 once the assembly code below has been executed?
A)
3
C)
7
D)
9
B)
4
LDR R1, 44
LDR R2, 48
ADD R1, R1, R2
CMP R1, #9
BNE end
STR R1, 48
end:
HALT
Memory address | Value
0 | 3
1 | 4

## Slide 11: What value is stored in memory address 52 once the assembly code below has been executed?
A)
0
C)
3
D)
4
B)
2
MOV R1, #2
CMP R1, #4
BGT end
STR R1, 52
end:
HALT
Memory address | Value
52 | 2

## Slide 12: What value is stored in memory address 48 once the assembly code below has been executed?
A)
0
C)
6
D)
4
B)
2
MOV R0, #0
loop:
ADD R0, R0, #2
CMP R0, #6
BNE loop
STR R0, 48
HALT

## Slide 13: What value is stored in memory address 52 once the assembly code below has been executed?
A)
3
C)
10
D)
0
B)
4
MOV R1, #3
CMP R1, #10
BNE IF
MOV R1, #4
STR R1, 52
B ELSE
IF:
STR R1, 52
ELSE:
HALT

## Slide 14: Answers by slide
D
D
D
A
A
C
C
C
C
B
C
A