## Slide 1: Wireless networking

## Slide 2: Learning objectives
Explain the following
  WiFi
  WiFi Components (Wireless Access Points & Wireless Network Adapter)
  SSID
  CSMA/CA
  How to secure wireless networks

## Slide 3: What is the purpose of WiFi
WiFi uses radio waves at a designated frequency (2.5 GHz or 5GHz) to transmit data and allows devices to be wirelessly networked.
International Wi-Fi standards are widely used so wireless devices should be able to be attached to any wireless network.

## Slide 4: Components for wireless networking
Wireless Access Point
A wireless access point (WAP) allows other wireless devices to connect to a network.
Has a range of the order of tens of metres
For most home wireless networks the WAP is integrated with the router.
Wireless Network Adapter
For a device (eg laptop) to connect to a wireless network it needs to have a wireless network adapter. The adapter can send and receive transmissions to the WAP so long as it is in range and operating on the same frequency.

## Slide 5: CSMA/CA
Wireless networks will often have multiple nodes each transmitting data packets. The purpose of the Carrier Sense Multiple Access / Collision Avoidance (CSMA/CA) protocol is to reduce collisions between data packets.
The CSMA/CA protocol:
The node listens to the network (channel) to determine whether data are being transmitted by another node.
If the network is busy then the node waits a random period of time until the next time it checks. The node keeps listening and waiting until the network becomes clear.
Once the network is clear the data can be transmitted.
The receiver sends an acknowledgement back to the sender.
If no acknowledgement is received the data need to be retransmitted.

## Slide 6: CSMA/CA with RTS/CTS
If more than one node send data at the same time, then a collision occurs. In this event the data will not be received so there will be no acknowledgement and the sending node will need to transmit.
To get around this problem we use CSMA/CA with RTS (Request to Send) / CTS (Clear to Send).

## Slide 7: Hidden nodes
Nodes on a wireless network are hidden from one another and communicate through the WAP
Nodes need to be within the broadcast range of the WAP otherwise they will not be on the network
However, nodes may be out of range of one another so they do not know when other nodes are transmitting
There is a way around this problem with the RTS/CTS signal
Node 1
Node 2
WAP
Node 3

## Slide 8: CSMA/CA with RTS/CTS Protocol
The node listens to the network (channel) to determine whether data are being transmitted by another node.
If the network is busy then the node waits a random period of time. The node keeps listening and waiting until the network becomes clear.
The node sends an RTS signal to the WAP, which returns a CTS signal once the network has been confirmed to be clear.
The node then transmits the data.
The receiver sends an acknowledgement back to the sender.
If no acknowledgement is received the data need to be retransmitted.

## Slide 9: Number of nodes
The greater the number nodes on a network, the greater the traffic and therefore the slower the network.

## Slide 10: How to secure wireless networks: MAC Address whitelist
A MAC address whitelist is a list that only allows devices with a specified MAC address to access the network. The MAC address of a device attempting to connect to the network is checked against the list. If the MAC address of the device is on the list then the device will be allowed to connect to the network otherwise it will not be able to access the network.

## Slide 11: How to secure wireless networks: Turn off the SSID broadcast
The SSID (Service Set Identifier) is the name given to a wireless network so that it can be identified. WiFi networks often broadcast their SSID. By turning off the SSID broadcast you are hiding the network, but you can still access if already know what the SSID of the network that you are trying to access is.

## Slide 12: How to secure wireless networks: Encryption
WEP (Wired Equivalent Privacy), WAP (WiFi Protected Access), WAP2 and WAP3 are the principal security protocols used to encrypt the data between the network adaptor and the access point. Therefore if any of the packets are intercepted the packets will at least be encrypted.
WEP – Has been cracked.
WAP – Supersedes WEP
WAP2 and WAP3 offers the best security of all

## Slide 13: How to secure wireless networks: Passcode
Passcodes can be added to WiFi networks to prevent unauthorised access to the networks.
Passcodes also serve as the key for the encryption

## Slide 14: Plenary
Describe how CSMA/CA works
Explain 3 ways how you would make a WiFi network more secure.
What hardware is needed for Wi Fi?

## Slide 15: AQA past papers
A level 2018 Paper 2 Q13
AS level 2016 P2 Q7
A specimen P2 Q7
AS Specimen P2 Q4

## Slide 16: Homework
Identify the steps required for CSMA/CA with RTS/CTS Protocol.
Do this from memory, then look at you notes to see whether or not you are correct.
Write down any steps you missed/got wrong in a different colour pen