## Slide 1: Starter: Create the Boolean algebra expressions from the Truth Table
..
Input A | Input B | Input C | Input D | Output
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0

## Slide 2: Karnaugh Maps

## Slide 3: Learning objectives
Use Karnaugh maps to simplify Boolean expressions.
Simplify Boolean expressions with two, three and four inputs.

## Slide 4: Karnaugh Maps
Karnaugh maps are a means of simplifying Boolean algebra expressions
If there are a large number of variables, it can take a long time working through the algebra to simplify the expressions.
Karnaugh maps offer a quicker way of simplifying expressions.

## Slide 5: Truth table versus Karnaugh Maps
A Karnaugh map is a truth table transformed into a 2D grid.
Variables are given along the dimensions.
When there are more than two inputs, multiple inputs are represented along each dimension.
Karnaugh maps allows us to easily find groups of 1’ s or 0’s.
The cells are ordered by Grey code, that is only 1 bit changes between cells next to one another.
For instance, in the case of a four-input column or row, Instead of 00, 01, 10, 11, as we might expect, the order is 00,01,11,10. ie the 11 and 10 are swapped around.

## Slide 6: Example truth table versus Karnaugh Maps: Two variables
A | B | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
A \ B | 0 | 1
0 | 0 | 1
1 | 0 | 1
Truth Table
Corresponding Karnaugh Map

## Slide 7: Example truth table versus Karnaugh Maps: Three variables
A | B | C | Output
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 1 | 1 | 1
A \ BC | 0 0 | 0 1 | 1 1 | 1 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 0
Truth Table
Corresponding Karnaugh Map
There are 2 variables along one of the dimensions in order to accommodate the 3 variables. It does not matter which variables are combined along the same dimension. In this example BC are combined but it could be AB or AC if we wished
There are two overlapping groups in this example.
The order of the cells is 00, 01, 11, 10

## Slide 8
A | B | C | D | Output
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0
0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
AB \ CD | 0 0 | 0 1 | 1 1 | 1 0
00 | 0 | 1 | 1 | 0
01 | 0 | 1 | 1 | 0
11 | 0 | 0 | 1 | 0
10 | 0 | 0 | 0 | 0
Corresponding Karnaugh Map
Example truth table versus Karnaugh Maps: Four variables
The order of the cells is 00, 01, 11, 10
There are 2 variables along each of the dimensions.

## Slide 9: Grouping
Draw boxes around groups of adjacent 1s.
Boxes must only contain 1s
Boxes must be square or rectangle.
Boxes must contain a number of cells to the powers of 2 (eg 1,2,4,8).
Boxes can overlap
Boxes must be as large as possible but also conform to the requirements stated above
Boxes can be joined together using the OR operator

## Slide 10: Example 1: Two input Karnaugh Maps
A | B | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A \ B | 0 | 1
0 | 0 | 1
1 | 1 | 1
Truth Table
Corresponding Karnaugh Map
When A = 1 then the output is 1
When B = 1 then the output is 1
Thus the equivalent Boolean algebra expression is:
Combining both groups together using the OR operator we get:
A + B

## Slide 11: Exercise: Convert the truth tables to Karnaugh maps and find the equivalent Boolean algebra expression
A | B | Output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
A | B | Output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
A | B | Output
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
a) b) c)

## Slide 12: Exercise: Convert the truth tables to Karnaugh maps and find the equivalent Boolean algebra expression - Answers
A | B | Output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
A | B | Output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
A | B | Output
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
a) b) c)
A \ B | 0 | 1
0 | 0 | 0
1 | 1 | 1
A \ B | 0 | 1
0 | 0 | 0
1 | 1 | 0
A \ B | 0 | 1
0 | 1 | 0
1 | 0 | 1

## Slide 13: Example 2: Three input Karnaugh Maps
A \ BC | 0 0 | 0 1 | 1 1 | 1 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1
Corresponding Karnaugh Map
In the red group both A and B are 0. The value of C has no effect.
In the green group both A and B are 1. The value of C has no effect.
Join both groups together using the OR operator
A | B | C | Output
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 1 | 0 | 1
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 1

## Slide 14: Exercise: Convert the truth table to Karnaugh maps and find the equivalent Boolean algebra expression
 |  | C | Output
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 1 | 1 | 1
 |  | C | Output
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 1 | 1 | 1
A \ BC | 0 0 | 0 1 | 1 1 | 1 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 0
Truth Table
Corresponding Karnaugh Map
When A = 0 then the output is 1, therefore the Boolean expression is
When both B AND C are 1 then the output is 1
Therefore the expression is:

## Slide 15: Exercise: Convert the truth table to Karnaugh maps and find the equivalent Boolean algebra expression
 |  |  | Output
0 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 1 | 0 | 0
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 1 | 1 | 0
 |  |  | Output
0 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 1 | 0 | 0
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 1 | 1 | 0
A \ BC | 0 0 | 0 1 | 1 1 | 10
0 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0
Truth Table
Corresponding Karnaugh Map
The expression is:

## Slide 16: Example 3: Four input Karnaugh Maps
AB \ CD | 0 0 | 0 1 | 1 1 | 10
0 0 | 0 | 1 | 1 | 0
0 1 | 0 | 1 | 1 | 0
1 1 | 0 | 0 | 1 | 1
1 0 | 0 | 0 | 1 | 1
Corresponding Karnaugh Map
When A = 0 and D=1 then the output is 1, therefore the expression Boolean expression is:
For the second group both A and C are 1 so:
Combining:
A | B | C | D | Output
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1
0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1

## Slide 17: Exercise: Given the following Karnaugh Mapz find the Boolean expression
AB \ CD | 0 0 | 0 1 | 1 1 | 10
0 0 | 1 | 0 | 0 | 0
0 1 | 1 | 0 | 0 | 0
1 1 | 1 | 0 | 1 | 0
1 0 | 1 | 0 | 1 | 0
AB \ CD | 0 0 | 0 1 | 1 1 | 10
0 0 | 0 | 0 | 1 | 1
0 1 | 0 | 0 | 1 | 1
1 1 | 0 | 0 | 0 | 1
1 0 | 0 | 1 | 1 | 1

## Slide 18: Overlapping Edge
AB \ CD | 0 0 | 0 1 | 1 1 | 1 0
0 0 | 0 | 1 | 1 | 0
0 1 | 1 | 0 | 0 | 1
1 1 | 1 | 0 | 0 | 1
1 0 | 0 | 1 | 1 | 0
The edges of the Karnaugh maps overlap from left and right and top and bottom.
A | B | C | D | Output
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1
0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1
0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0

## Slide 19: Exercise: Given the following Karnaugh Map find the Boolean expression
AB \ CD | 0 0 | 0 1 | 1 1 | 10
0 0 | 0 | 0 | 0 | 0
0 1 | 1 | 0 | 0 | 1
1 1 | 0 | 0 | 0 | 0
1 0 | 0 | 0 | 0 | 0
AB \ CD | 0 0 | 0 1 | 1 1 | 10
0 0 | 1 | 0 | 0 | 1
0 1 | 0 | 0 | 0 | 0
1 1 | 0 | 0 | 0 | 0
1 0 | 1 | 0 | 0 | 1

## Slide 20: Plenary: Given the following Karnaugh Map find the Boolean expression
.C
AB \ CD | 0 0 | 0 1 | 1 1 | 10
0 0 | 0 | 0 | 0 | 0
0 1 | 1 | 0 | 0 | 1
1 1 | 0 | 1 | 1 | 1
1 0 | 0 | 0 | 1 | 1
A \ B | 0 | 1
0 | 0 | 1
1 | 0 | 0
A \ BC | 0 0 | 0 1 | 1 1 | 10
0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1