## Slide 1: Starter: Boolean Identities Practice
Alternatively use: dq-boolean-identities-10.pptx

## Slide 2: Half Adder, Full Adder and D-Type Flip Flop

## Slide 3: Learning Objectives
Examine a range of digital circuits and explain how they work:
  Half adder
  Full adder
  D-type flip flops

## Slide 4: Half Adder
A half adder adds two bits together.
It is made up of an AND and an XOR gate.
It has two bits as inputs (A and B). These are the two bits that we wish to add together.
It has two bit as the outputs (S and C). S is the sum (S) of the addition and (C) is the carry bit.
Input A |  | Input B |  | C (carry) | S (sum)
0 | + | 0 | = | 0 | 0
1 | + | 0 | = | 0 | 1
0 | + | 1 | = | 0 | 1
1 | + | 1 | = | 1 | 0

## Slide 5: Full Adder
A full adder adds 3 bits together, one of which is the carry bit.
It is made up of an AND, XOR and OR gates and contains two half adders
Two bits are output: the sum (S) and the carry (C) bits
A |  | B |  | Cin |  | Cout | S | D | E | F
0 | + | 0 | + | 0 | = | 0 | 0 | 0 | 0 | 0
0 | + | 0 | + | 1 | = | 0 | 1 | 0 | 0 | 0
0 | + | 1 | + | 0 | = | 0 | 1 | 1 | 0 | 0
0 | + | 1 | + | 1 | = | 1 | 0 | 1 | 1 | 0
1 | + | 0 | + | 0 | = | 0 | 1 | 1 | 0 | 0
1 | + | 0 | + | 1 | = | 1 | 0 | 1 | 1 | 0
1 | + | 1 | + | 0 | = | 1 | 0 | 0 | 0 | 1
1 | + | 1 | + | 1 | = | 1 | 1 | 0 | 0 | 1

## Slide 6: Binary Adder
A binary adder consists of a sequence of full adders
The output carry bit from one full adder is the input into the next
we can add together binary numbers of any number of bits according to the number of full address that we chain together
In this example we can add 2 three bits binary numbers

## Slide 7: Binary Adder Circuit
1 0 1
+ 0 1 1
+ 1 1 0
1 0 0 0
A3 A2 A1
+ B3 B2 B1
+ C3 C2 C1
C4 S3 S2 S1
4
1
1
0
0
0
1
1
0
1
0
1
0
1

## Slide 8: Binary Adder Circuit
1 0 1
+ 0 1 1
+ 1 1 0
1 0 0 0
A3 A2 A1
+ B3 B2 B1
+ C3 C2 C1
C4 S3 S2 S1
4

## Slide 9: 4-bit Binary Adder
A3 A2 A1 A0
+ B3 B2 B1 B0
+ C3 C2 C1 C0
C4 S3 S2 S1 S0

## Slide 10: D-type Flip Flop
D type flip-flops are used for controlled delay in a circuit.
This is the basis for storing data in memory registers.
D (delay)-type flip flops are used to store one bit and flip between two states: 1 and 0.
The inputs are a control value (0 or 1) and also a clock value (0 or 1) that changes the state at a regular rate.
Q and Q’ are the inverse of each other
The output Q can only change when the clock value is 1.
When the clock value is 0 there is no change in Q
D-type flip-flop
Input data, D
Input clock
Output Q
Output Not Q

## Slide 11: D Type Flip Flop - circuit
D | Clock | Q | Not Q
0 | 0 | No change | No change
1 | 0 | No change | No change
0 | 1 | 0 | 1
1 | 1 | 1 | 0
D Type flip-flop is made up of 5 NAND gates, though 1 acts as a NOT gates as both inputs are the same
Has a feedback loop

## Slide 12: Level Triggered D Type Flip Flop
D | Clock | Q | Not Q
0 | 0 | No change | No change
1 | 0 | No change | No change
0 | 1 | 0 | 1
1 | 1 | 1 | 0
Delay

## Slide 13: Exercise 1: Draw the output plot for the D type flip flop
See flip-flops.docx

## Slide 14: Exercise 1: Draw the output plot for the D type flip flop - Answer

## Slide 15: Edge Triggered D-type Flip Flop
The problem with the D type flip-flop is if the input clock is 1 and the D changes from 0 to 1 or vice versa, Q will change in response. This effect is known as ripple through and is undesirable.

## Slide 16: Ripple through effect
The D-Type flip flop has no effect
In this example.
D | Clock | Q | Not Q
0 | 0 | No change | No change
1 | 0 | No change | No change
0 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 17: Edge Triggered D-type Flip Flop
To solve this we use a positive edge triggered flip-flop.
For a positive edge triggered flip-flop the output state can only change when the clock changes from 0 to 1. If D is in the same state as it was on the previous edge then the output is unchanged. However if D has changed state, the output state will change to the value of D.

## Slide 18: Edge triggered D-Type flip flop example
D | Clock | Q
0 |  | 0
1 |  | 1
Edge Trigger
Delay

## Slide 19: Edge versus level triggered flip flop
Level triggered flip flop with ripple through
Edge triggered flip flop without ripple through

## Slide 20: Exercise 2a: Draw the output plot for a level triggered D type flip flop

## Slide 21: Exercise 2b: Draw the output plot for an edge triggered D type flip flop

## Slide 22: Exercise 2a: Draw the output plot for a level triggered D type flip flop - Answer

## Slide 23: Exercise 2b: Draw the output plot for an edge triggered D type flip flop - Answer

## Slide 24: Exercise 3a: Draw the output plot for a level triggered D type flip flop

## Slide 25: Exercise 3b: Draw the output plot for an edge triggered D type flip flop

## Slide 26: Exercise 3a: Draw the output plot for a level triggered D type flip flop - Answer

## Slide 27: Exercise 3b: Draw the output plot for an edge triggered D type flip flop - Answer

## Slide 28: Plenary
Draw the circuit for the half adder.
What is the purpose of the edge-triggered D-type flip flop?
Create a half adder, full adder and D-type flip-flop using https://logic.ly/demo/