## Slide 1
Logic Gates and Logic Circuits
A LEVEL COMPUTER SCIENCE
Chapter
4

## Slide 2
Cambridge International AS Level Computer Science (9618) – Revision Notes
This pack is intended for students to who are taking CIE AS Level in Computer Science, either in preparation for their AS exam, or more likely alongside year 2 of the course to improve fluency, recall and pace on AS topics. It could be used as lesson starters, or supplied to students for independent use.
Logic Gates and Logic Circuits

## Slide 3
Logic Gates
A LEVEL COMPUTER SCIENCE
Chapter
4
Purpose: They perform logical functions, which help in the processing and manipulation of binary data in digital circuits and computer systems.

## Slide 4
Chapter
Outline
Terminology
4.1
4.2
Truth Table
and
4.3
Logic Gates
Boolean Operators
  Logic Propositions
  Problem Statement
  Logic Expression
Logic Circuit
Construct a logic expression from a problem statement
Constructing a logic circuit from a problem statement or logic expression
Worked Example
4.4
Construct a truth table from a logic circuit
Construct a logic circuit based on a truth table

## Slide 5
4.1 Terminology
Logic Proposition
A logic proposition is a statement that can be evaluated as either true or false, but not both, based on factual or theoretical conditions.
Eg. The Sun rises in the east.

## Slide 6
4.1 Terminology
Problem Statement
When the traffic light isn't green and the pedestrian signal is on, Stop your vehicle and yield to pedestrians.
Highlighter
An outcome that relies on either a single logic proposition or a combination of two or more logic propositions.

## Slide 7
4.1 Terminology
Problem Statement
Highlighter
An outcome that relies on either a single logic proposition or a combination of two or more logic propositions.
When the traffic light isn't green and the pedestrian signal is on,
Stop your vehicle and yield to pedestrians.
Logic Proposition 1
Logic Proposition 2
Outcome

## Slide 8
Subtopic 1
Introduction
4.2 Boolean Operators
When the traffic light isn't green AND the pedestrian signal is on,
Stop your vehicle and yield to pedestrians.
Boolean Operator

## Slide 9
Subtopic 1
Introduction
A boolean operator is a logical operator that performs operations on boolean values (true or false) to produce a boolean result.
The three boolean operators are:
4.2 Boolean Operators
AND
OR
NOT
A
B
= True
= True
=
TRUE
B
= True
= False
A
=
TRUE
Statement
= FALSE
A
=
TRUE

## Slide 10
Subtopic 1
Logic Expression
4.2 Boolean Operators
A logic expression is a combination of logical operators and statements that evaluates to a boolean value (either true or false) based on the given conditions or rules.
When the traffic light isn't green and the pedestrian signal is on,
Stop your vehicle and yield to pedestrians.

## Slide 11
Subtopic 1
Logic Expression
Can be rewritten to
4.2 Boolean Operators
STOP_VEHICLE =
NOT (traffic light is green = TRUE)
AND (pedestrian signal on = TRUE)
A logic expression is a combination of logical operators and statements that evaluates to a boolean value (either true or false) based on the given conditions or rules.
When the traffic light isn't green and the pedestrian signal is on,
Stop your vehicle and yield to pedestrians.

## Slide 12
Subtopic 1
Other boolean operators
The following operators are also commonly used:
4.2 Boolean Operators
NAND
NOR
XOR
A
B
= False
= False
=
TRUE
B
= False
= False
A
=
TRUE
TRUE
NOT + AND
NOT + OR
EITHER OR
B
= True
= False
A
=
= True
= False

## Slide 13
4.3 Truth Tables and Logic Gates
Introduction
A truth table is a table that displays
all possible input combinations
and their corresponding output values
in logic or Boolean expressions.
An element within a logic circuit that performs functions consistent with those of a Boolean Operator.
INPUT
A
X
0
0
OUTPUT
B
0
1
1
0
1
1
Truth Table
Logic Gate

## Slide 14
AND Operator
4.3 Truth Tables and Logic Gates
AND gate
INPUT
A
X
0
0
Truth Table
OUTPUT
B
0
1
1
0
1
1
0
0
0
1
A
B
X
The AND date takes the inputs A and B and produces the output, X.
If both inputs are 1, then the output will be 1, but otherwise the output will be 0.

## Slide 15
OR Operator
4.3 Truth Tables and Logic Gates
OR gate
Truth Table
A
B
X
The OR gate takes two inputs, A and B, and produces output X. If either or both inputs is 1, the output will be 1.
INPUT
A
X
0
0
OUTPUT
B
0
1
1
0
1
1
0
1
1
1

## Slide 16
NOT Operator
4.3 Truth Tables and Logic Gates
NOT gate
Truth Table
The NOT gate takes a single input and produces the opposite of that input in a single output
A
X
INPUT
A
X
0
1
1
0
OUTPUT

## Slide 17
NAND Operator
4.3 Truth Tables and Logic Gates
NAND gate
Truth Table
NAND (NOT + AND). It will only give an output of 0 if both inputs are 1.
A
B
X
AND Gate
NOT Gate
INPUT
A
X
0
0
AND
B
0
1
1
0
1
1
X
0
0
0
1
NAND
Negation of
AND
1
1
1
0

## Slide 18
NOR Operator
4.3 Truth Tables and Logic Gates
NOR gate
NOR (NOT + OR). Produces an output if both inputs A and B are 0.
INPUT
A
X
0
0
Truth Table
OR
B
0
1
1
0
1
1
X
0
1
1
1
NOR
Negation of
OR
1
0
0
0
A
X
B
OR Gate
NOT Gate

## Slide 19
XOR Operator
4.3 Truth Tables and Logic Gates
XOR gate
XOR (Exclusive OR). The output X is 1 when either (but not both) of the A or B inputs is 1.
A
B
X
INPUT
A
X
0
0
Truth Table
OUTPUT
B
0
1
1
0
1
1
0
1
1
0

## Slide 20
4.4 Worked Example
You are designing a computer game character selection system. Players can choose their characters based on the following criteria:
Worked Example 1: Construct a logic expression from a problem statement
Firstly, they should have achieved a high score of at least 100 points. Secondly, they must have successfully completed a minimum of three game levels. Thirdly, they need to have unlocked a special in-game achievement. However, there's an exception for premium members; if a player is a premium member, they can access exclusive characters even if they have not unlocked the special in-game achievement.
These four conditions collectively determine a player's eligibility to access and play as the exclusive characters in the game.

## Slide 21
4.4 Worked Example
Identify the conditions in a statement that can have true or false values
Worked Example 1: Construct a logic expression from a problem statement
Firstly, they should have achieved a high score of at least 100 points.
Secondly, they must have successfully completed a minimum of three game levels.
Thirdly, they need to have unlocked a special in-game achievement. However, there's an exception for premium members; if a player is a premium member, they can access exclusive characters even if they have not unlocked the special in-game achievement.

## Slide 22
4.4 Worked Example
Change each condition into symbols
Worked Example 1: Construct a logic expression from a problem statement
A - achieved a high score of at least 100 points.
B - completed a minimum of three game levels.
C - unlocked a special in-game achievement.
D - premium member

## Slide 23
4.4 Worked Example
Construct the logical expression
Worked Example 1: Construct a logic expression from a problem statement
A AND B AND (C OR D)

## Slide 24
4.4 Worked Example
A university will only admit a student in if the student fulfils the following criteria:
Worked Example 2: Constructing a logic circuit from a problem statement or logic expression
  The student has achieved at least 3A* in the A-level exam
  Two of the following conditions must also apply
    The student has demonstrated extensive leadership experience
    The student has gotten 2 recommendation letters from field experts
    The student has a portfolio of projects deemed impressive

## Slide 25
4.4 Worked Example
Worked Example 2: Constructing a logic circuit from a problem statement or logic expression
A - The student has achieved at least 3A* in the A-level exam
Two of the following conditions must also apply
B - The student has extensive leadership experience
C - The student has gotten 2 recommendation letters from field experts
D - The student has a portfolio deemed impressive

## Slide 26
4.4 Worked Example
Worked Example 2: Constructing a logic circuit from a problem statement or logic expression
A - The student has achieved at least 3A* in the A-level exam
Two of the following conditions must also apply
B - The student has extensive leadership experience
C - The student has gotten 2 recommendation letters from field experts
D - The student has a portfolio deemed impressive
A AND

## Slide 27
4.4 Worked Example
Worked Example 2: Constructing a logic circuit from a problem statement or logic expression
A - The student has achieved at least 3A* in the A-level exam
Two of the following conditions must also apply
B - The student has extensive leadership experience
C - The student has gotten 2 recommendation letters from field experts
D - The student has a portfolio deemed impressive
A AND
(( ) OR
( ) OR
( ))

## Slide 28
4.4 Worked Example
Worked Example 2: Constructing a logic circuit from a problem statement or logic expression
A - The student has achieved at least 3A* in the A-level exam
Two of the following conditions must also apply
B - The student has extensive leadership experience
C - The student has gotten 2 recommendation letters from field experts
D - The student has a portfolio deemed impressive
A AND
((B AND C) OR
(B AND D) OR
(C AND D))

## Slide 29
4.4 Worked Example
Worked Example 2: Constructing a logic circuit from a problem statement or logic expression
A AND ((B AND C) OR (B AND D) OR (C AND D))
Based on a logic expression, create a circuit.

## Slide 30
4.4 Worked Example
Worked Example 2: Constructing a logic circuit from a problem statement or logic expression
A AND ((B AND C) OR (B AND D) OR (C AND D))
A
B
C
D

## Slide 31
4.4 Worked Example
Worked Example 2: Constructing a logic circuit from a problem statement or logic expression
A AND ((B AND C) OR (B AND D) OR (C AND D))
A
B
C
D

## Slide 32
4.4 Worked Example
Worked Example 2: Constructing a logic circuit from a problem statement or logic expression
A AND ((B AND C) OR (B AND D) OR (C AND D))
A
B
C
D

## Slide 33
4.4 Worked Example
Worked Example 2: Constructing a logic circuit from a problem statement or logic expression
A AND ((B AND C) OR (B AND D) OR (C AND D))
A
B
C
D

## Slide 34
4.4 Worked Example
Worked Example 3: Construct a truth table from a logic circuit
A
B
C
A
0
0
B
0
0
0
1
0
1
C
0
1
0
1
1
1
0
0
1
1
1
1
0
1
0
1
INPUT
Intermediate Output
OUTPUT

## Slide 35
4.4 Worked Example
Worked Example 3: Construct a truth table from a logic circuit
A
B
C
Step 1: Identify all the intermediate outputs
P
Q
R
S

## Slide 36
4.4 Worked Example
Worked Example 3: Construct a truth table from a logic circuit
B
0
0
1
1
C
0
1
0
1
0
0
1
A
0
0
0
0
1
1
1
1
1
0
1
0
1
INPUT
Intermediate Output
OUTPUT
A
B
C
P
Q
R
S
Step 2: Identify the result of each intermediate output
P

## Slide 37
4.4 Worked Example
Worked Example 3: Construct a truth table from a logic circuit
B
0
0
1
1
C
0
1
0
1
0
0
1
A
0
0
0
0
1
1
1
1
1
0
1
0
1
INPUT
Intermediate Output
OUTPUT
A
B
C
P
Q
R
S
Step 2: Identify the result of each intermediate output
P
1
1
1
1
0
0
0
0

## Slide 38
4.4 Worked Example
Worked Example 3: Construct a truth table from a logic circuit
A
0
0
0
0
1
1
1
1
B
0
0
1
1
C
0
1
0
1
0
0
1
1
0
1
0
1
INPUT
Intermediate Output
OUTPUT
A
B
C
P
Q
R
S
Step 2: Identify the result of each intermediate output
P
1
1
1
1
0
0
0
0
Q

## Slide 39
4.4 Worked Example
Worked Example 3: Construct a truth table from a logic circuit
A
0
0
0
0
1
1
1
1
B
0
0
1
1
C
0
1
0
1
0
0
1
1
0
1
0
1
INPUT
Intermediate Output
OUTPUT
A
B
C
P
Q
R
S
Step 2: Identify the result of each intermediate output
P
1
1
1
1
0
0
0
0
Q
0
0
0
1
0
0
0
1

## Slide 40
4.4 Worked Example
Worked Example 3: Construct a truth table from a logic circuit
A
0
0
0
0
C
0
1
0
1
1
1
1
1
B
0
0
1
1
0
0
1
1
0
1
0
1
INPUT
Intermediate Output
OUTPUT
A
B
C
P
Q
R
S
Step 2: Identify the result of each intermediate output
P
1
1
1
1
0
0
0
0
Q
0
0
0
1
0
0
0
1
R

## Slide 41
4.4 Worked Example
Worked Example 3: Construct a truth table from a logic circuit
A
0
0
0
0
C
0
1
0
1
1
1
1
1
B
0
0
1
1
0
0
1
1
0
1
0
1
INPUT
Intermediate Output
OUTPUT
A
B
C
P
Q
R
S
Step 2: Identify the result of each intermediate output
P
1
1
1
1
0
0
0
0
Q
0
0
0
1
0
0
0
1
R
1
1
1
1
0
0
1
1

## Slide 42
4.4 Worked Example
Worked Example 3: Construct a truth table from a logic circuit
A
0
0
0
0
C
0
1
0
1
1
1
1
1
0
1
0
1
INPUT
Intermediate Output
OUTPUT
A
B
C
P
Q
R
S
Step 2: Identify the result of each intermediate output
B
0
0
1
1
0
0
1
1
P
1
1
1
1
0
0
0
0
Q
0
0
0
1
0
0
0
1
R
1
1
1
1
0
0
1
1
S

## Slide 43
4.4 Worked Example
Worked Example 3: Construct a truth table from a logic circuit
A
0
0
0
0
C
0
1
0
1
1
1
1
1
0
1
0
1
INPUT
Intermediate Output
OUTPUT
A
B
C
P
Q
R
S
Step 2: Identify the result of each intermediate output
B
0
0
1
1
0
0
1
1
P
1
1
1
1
0
0
0
0
Q
0
0
0
1
0
0
0
1
R
1
1
1
1
0
0
1
1
S
1
1
1
0
1
1
1
0

## Slide 44
4.4 Worked Example
Worked Example 3: Construct a truth table from a logic circuit
A
0
0
0
0
C
0
1
0
1
1
1
1
1
0
1
0
1
INPUT
Intermediate Output
OUTPUT
A
B
C
P
Q
R
S
Step 3: Find out the final output.
B
0
0
1
1
0
0
1
1
P
1
1
1
1
0
0
0
0
Q
0
0
0
1
0
0
0
1
R
1
1
1
1
0
0
1
1
S
1
1
1
0
1
1
1
0
X

## Slide 45
4.4 Worked Example
Worked Example 3: Construct a truth table from a logic circuit
A
0
0
0
0
C
0
1
0
1
1
1
1
1
0
1
0
1
INPUT
Intermediate Output
OUTPUT
A
B
C
P
Q
R
S
Step 3: Find out the final output.
B
0
0
1
1
0
0
1
1
P
1
1
1
1
0
0
0
0
Q
0
0
0
1
0
0
0
1
R
1
1
1
1
0
0
1
1
S
1
1
1
0
1
1
1
0
X
0
0
0
1
1
1
0
1

## Slide 46
4.4 Worked Example
Step 1: Identify rows in which the output is 1
Step 2: Form a logical expression from each of these rows using an OR statement
Step3: Combine all the logical expressions created using an AND statement
Worked Example 4: Construct a logic circuit based on a truth table
A
0
0
B
0
0
0
1
0
1
C
0
1
0
1
1
1
0
0
1
1
1
1
0
1
0
1
INPUT
OUTPUT
1
0
0
0
0
1
1
0
X

## Slide 47
4.4 Worked Example
Step 1: Identify rows in which the output is 1
Step 2: Form a logical expression from each of these rows using an OR statement
Step3: Combine all the logical expressions created using an AND statement
Worked Example 4: Construct a logic circuit based on a truth table
A
0
B
0
0
1
0
1
C
1
0
1
1
0
1
1
0
1
INPUT
OUTPUT
0
0
0
1
0
0
0
0
1
0
1
1
1
0
1
1
0
X

## Slide 48
4.4 Worked Example
Step 1: Identify rows in which the output is 1
Step 2: Form a logical expression from each of these rows using an AND statement
*if the input value is a 0, we add a NOT gate (eg. NOT A)
Step3: Combine all the logical expressions created using an OR statement
Worked Example 4: Construct a logic circuit based on a truth table
A
0
B
0
0
1
0
1
C
1
0
1
1
0
1
1
0
1
INPUT
OUTPUT
0
0
0
1
0
0
0
0
1
0
1
1
1
0
1
1
0
X
NOT A AND NOT B AND NOT C
A AND NOT B AND C
A AND B AND NOT C

## Slide 49
4.4 Worked Example
Step 1: Identify rows in which the output is 1
Step 2: Form a logical expression from each of these rows using an AND statement
*if the input value is a 0, we add a NOT gate (eg. NOT A)
Step3: Combine all the logical expressions created using an OR statement
Worked Example 4: Construct a logic circuit based on a truth table
A
0
B
0
0
1
0
1
C
1
0
1
1
0
1
1
0
1
INPUT
OUTPUT
0
0
0
1
0
0
0
0
1
0
1
1
1
0
1
1
0
X
NOT A AND NOT B AND NOT C
A AND NOT B AND C
A AND B AND NOT C

## Slide 50
4.4 Worked Example
Step 1: Identify rows in which the output is 1
Step 2: Form a logical expression from each of these rows using an AND statement
*if the input value is a 0, we add a NOT gate (eg. NOT A)
Step3: Combine all the logical expressions created using an OR statement
Worked Example 4: Construct a logic circuit based on a truth table
A
0
B
0
0
1
0
1
C
1
0
1
1
0
1
1
0
1
INPUT
OUTPUT
0
0
0
1
0
0
0
0
1
0
1
1
1
0
1
1
0
X
(NOT A AND NOT B AND NOT C)
(A AND NOT B AND C)
(A AND B AND NOT C)
OR
OR

## Slide 51
4.4 Worked Example
Worked Example 4: Construct a logic circuit based on a truth table
(NOT A AND NOT B AND NOT C)
(A AND NOT B AND C)
(A AND B AND NOT C)
OR
OR