## Slide 1
Cambridge International A Level Computer Science (9618) – Revision Notes
This pack is intended for students to who are taking CIE A Level in Computer Science, either in preparation for their A Level exam, or more likely alongside year 2 of the course to improve fluency, recall and pace on AS & A topics. It could be used as lesson starters, or supplied to students for independent use.
Digital Logic and Boolean Algebra

## Slide 2
Digital Logic and Boolean Algebra
AS & A Level Computer Science 9618
Chapter
19

## Slide 3
Chapter
Outline
Fundamentals of Logic Circuits
19.1
Designing Sequential Logic Circuits
19.2
Introduction to Boolean Algebra
19.3
Practical Applications of Boolean Algebra
Karnaugh maps
(K-maps)
19.5
19.4

## Slide 4
19.1 Fundamentals of Logic Circuits
1
1
10
Half adder
A half adder performs the addition of two single binary digits, generating the sum and carry output.
+
1
1 bit half adder circuitry
Bit 1
Bit 2
Sum
Carry

## Slide 5
Input | Input | Output | Output
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Half adder
Truth Table for a half adder:
19.1 Fundamentals of Logic Circuits

## Slide 6
Input | Input | Output | Output
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Half adder
The S output can be constructed using an XOR gate.
19.1 Fundamentals of Logic Circuits

## Slide 7
Input | Input | Output | Output
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Half adder
The C output can be constructed using an AND gate.
19.1 Fundamentals of Logic Circuits

## Slide 8
Universal Gates
The NAND Gates and NOR Gates are universal gates. Any logical circuit can be constructed using these gates.
Circuit manufacturers prefer using universal gates, like NAND or NOR gates, to create adder circuits due to their versatility and the ability to construct all other logic gates, minimizing the number of distinct components needed for various circuit designs.
A
B
X
AND Gate
NOT Gate
A
X
B
OR Gate
NOT Gate
19.1 Fundamentals of Logic Circuits

## Slide 9
Half adder (using NAND Gates)
19.1 Fundamentals of Logic Circuits

## Slide 10
Full adder
11
11
110
+
1
A full adder is necessary because it can handle the addition of three inputs (two bits and a carry) to produce a sum and carry output, allowing for accurate arithmetic calculations in multi-bit operations, which a half adder alone cannot accomplish.
1
19.1 Fundamentals of Logic Circuits

## Slide 11
Input | Input | Input | Output | Output
A | B | C in | S | C out
Full adder
Truth table for a full adder:
0
0
0
0
0
1
0
1
0
0
1
1
1
0
0
1
0
1
1
1
0
1
1
1
0
1
1
0
1
0
0
1
0
0
0
1
0
1
1
1
19.1 Fundamentals of Logic Circuits

## Slide 12
Full adder
Truth table for a full adder:
19.1 Fundamentals of Logic Circuits

## Slide 13
Full adder
8-bit full adder
19.1 Fundamentals of Logic Circuits

## Slide 14
Subtopic 1
Types of logic circuits
19.2 Designing Sequential Logic Circuits
Combinational circuit
Sequential circuit
A digital circuit whose output at any given time is solely determined by its current inputs.
A digital circuit where the output is influenced not only by the current inputs but also by the circuit's previous state.

## Slide 15
Subtopic 1
Types of logic circuits
Combinational circuit
A digital circuit whose output at any given time is solely determined by its current inputs.
19.2 Designing Sequential Logic Circuits

## Slide 16
Subtopic 1
Sequential circuits
SR flip-flop
JK flip-flop
19.2 Designing Sequential Logic Circuits

## Slide 17
Subtopic 1
Sequential circuits
SR flip-flop
JK flip-flop
19.2 Designing Sequential Logic Circuits

## Slide 18
Subtopic 1
SR flip-flop - a two state device
Output of one circuit is the input of the other.
Either Q = 1 and Q’ = 0 or reverse
If R,S,Q, Q’ all have the value 0, it will be self contradictory.
A state with Q and Q’ both set to 1 is also self contradictory.
(Set Reset)
R
S
19.2 Designing Sequential Logic Circuits

## Slide 19
Subtopic 1
SR flip-flop - Truth Table
Input | Input | Initial State | Initial State | Final State | Final State
S | R | Q | Q’ | Q | Q’
0
0
1
0
1
0
1
0
1
0
1
0
0
1
0
0
0
1
0
0
0
1
0
1
1
0
0
1
1
0
0
1
0
1
0
1
19.2 Designing Sequential Logic Circuits

## Slide 20
Subtopic 1
SR flip-flop
Input | Input | Initial State | Initial State | Final State | Final State
S | R | Q | Q’ | Q | Q’
0
0
1
0
1
0
0
0
0
1
0
1
S = 0 , R = 0.
Self consistency state.
19.2 Designing Sequential Logic Circuits

## Slide 21
Subtopic 1
SR flip-flop
Input | Input | Initial State | Initial State | Final State | Final State
S | R | Q | Q’ | Q | Q’
1
0
1
0
1
0
1
0
0
1
0
1
S = 1 , R = 0.
Converts an unset state to a set state (SET).
19.2 Designing Sequential Logic Circuits

## Slide 22
Subtopic 1
SR flip-flop
Input | Input | Initial State | Initial State | Final State | Final State
S | R | Q | Q’ | Q | Q’
0
1
1
0
0
1
0
1
0
1
0
1
S = 0 , R = 1.
Converts an set state to a unset state (RESET).
19.2 Designing Sequential Logic Circuits

## Slide 23
Subtopic 1
SR flip-flop
Note that S and R cannot be 1 at the same time. You can’t reset and set at the same time. This would be contradictory.
Input | Input | Initial State | Initial State | Final State | Final State
S | R | Q | Q’ | Q | Q’
0
0
1
0
1
0
1
0
1
0
1
0
0
1
0
0
0
1
0
0
0
1
0
1
1
0
0
1
1
0
0
1
0
1
0
1
19.2 Designing Sequential Logic Circuits

## Slide 24
Subtopic 1
SR flip-flop
Q and Q’ cannot have the same state too. SR flip-flop is a two-state device.
Input | Input | Initial State | Initial State | Final State | Final State
S | R | Q | Q’ | Q | Q’
0
0
1
0
1
0
1
0
1
0
1
0
0
1
0
0
0
1
0
0
0
1
0
1
1
0
0
1
1
0
0
1
0
1
0
1
19.2 Designing Sequential Logic Circuits

## Slide 25
Subtopic 1
SR flip-flop
SR flip-flops are employed in creating the storage cells within RAM (Random Access Memory) where each flip-flop represents a single memory bit, storing data in the form of binary information (0s and 1s).
19.2 Designing Sequential Logic Circuits

## Slide 26
Subtopic 1
Sequential circuits
SR flip-flop
JK flip-flop
19.2 Designing Sequential Logic Circuits

## Slide 27
Subtopic 1
JK flip-flop
It is possible for a circuit to arrive at an uncertain state if inputs do not arrive quite at the same time. JK flip flop include a clock pulse input to give a better chance of synchronising inputs.
19.2 Designing Sequential Logic Circuits

## Slide 28
Subtopic 1
J | K | Clock | Q
0 | 0 |  | Q unchanged
1 | 0 |  | 1
0 | 1 |  | 0
1 | 1 |  | Q toggles
JK flip-flop (part of the truth table)
Set Input
Clear Input
When both J and K are 1, Q toggles. This makes JK flip flop a more reliable device because there is no invalid state (Unlike SR).
19.2 Designing Sequential Logic Circuits

## Slide 29
19.3 Introduction to Boolean Algebra
Notation
We can write A AND B like this:
A.B
We can write NOT A like this:
A
_
We can write A OR B like this:
A+B

## Slide 30
Boolean Algebra Laws - Identity
Law
AND form
OR form
Identity
1.A = A
TRUE AND (TRUE) = TRUE
TRUE AND (FALSE) = FALSE
FALSE OR (TRUE) = TRUE
FALSE OR (FALSE) = FALSE
0+A = A
19.3 Introduction to Boolean Algebra

## Slide 31
Boolean Algebra Laws - Null
Law
AND form
OR form
Null
0.A = 0
FALSE AND (TRUE) = FALSE
FALSE AND (FALSE) = FALSE
TRUE OR (TRUE) = TRUE
TRUE OR (FALSE) = TRUE
1 + A = 1
19.3 Introduction to Boolean Algebra

## Slide 32
Boolean Algebra Laws - Idempotent
Law
AND form
OR form
Idempotent
A.A = A
TRUE AND (TRUE) = TRUE
FALSE AND (FALSE) = FALSE
TRUE OR (TRUE) = TRUE
FALSE OR (FALSE) = FALSE
A + A = A
19.3 Introduction to Boolean Algebra

## Slide 33
Boolean Algebra Laws - Inverse
Law
AND form
OR form
Inverse
A.A = 0
TRUE AND (NOT TRUE) = FALSE
FALSE AND (NOT FALSE) = FALSE
TRUE OR (NOT TRUE) = TRUE
FALSE OR (NOT FALSE) = FALSE
A + A = 1
_
_
19.3 Introduction to Boolean Algebra

## Slide 34
Boolean Algebra Laws - Commutative
Law
AND form
OR form
Commutative
A.B = B.A
TRUE AND FALSE = FALSE AND TRUE
FALSE AND TRUE = TRUE AND FALSE
A+B = B+A
TRUE OR FALSE = FALSE OR TRUE
FALSE OR TRUE = TRUE OR FALSE
19.3 Introduction to Boolean Algebra

## Slide 35
Boolean Algebra Laws - Associative
Law
AND form
OR form
Associative
(A.B).C = A.(B.C)
(TRUE AND FALSE) AND TRUE =
TRUE AND (FALSE AND TRUE)
(A+B)+C = A+(B+C)
(TRUE OR FALSE) OR TRUE =
TRUE OR (FALSE OR TRUE)
19.3 Introduction to Boolean Algebra

## Slide 36
Boolean Algebra Laws - Distributive
Law
AND form
OR form
Distributive
A + B.C = (A+B) . (A + C)
TRUE OR FALSE AND TRUE =
(TRUE OR FALSE) AND (TRUE OR TRUE)
A.(B+C) = A.B + A.C
TRUE AND FALSE OR TRUE =
(TRUE AND FALSE) OR (TRUE AND TRUE)
19.3 Introduction to Boolean Algebra

## Slide 37
Boolean Algebra Laws - Absorption
Law
AND form
OR form
Absorption
A.(A+B) = A
A + A.B = A
TRUE AND (TRUE OR FALSE) = TRUE
TRUE OR (TRUE AND FALSE) = TRUE
19.3 Introduction to Boolean Algebra

## Slide 38
Boolean Algebra Laws - De Morgan’s
Law
AND form
OR form
De Morgan’s
A.B = A + B
A + B = A . B
NOT (TRUE OR FALSE) = NOT TRUE AND NOT FALSE
NOT (TRUE AND FALSE) = NOT TRUE OR NOT FALSE
19.3 Introduction to Boolean Algebra

## Slide 39
Boolean Algebra Laws - Double Complement
Law
Double Complement
A = A
NOT NOT TRUE = TRUE
_
_
19.3 Introduction to Boolean Algebra

## Slide 40
Using Boolean algebra to simplify an equation
A + A.B
_
= A + B
Prove ➡️
19.3 Introduction to Boolean Algebra

## Slide 41
Using Boolean algebra to simplify an equation
A + A.B
_
= A + B
Absorption
A+(A.B) + A.B
_
A + A.B = A
19.3 Introduction to Boolean Algebra

## Slide 42
Using Boolean algebra to simplify an equation
A + A.B
_
= A + B
Absorption
A+(A.B) + A.B
A+(B.A) + B.A
Commutative
A.B = B.A
_
_
A + A.B = A
19.3 Introduction to Boolean Algebra

## Slide 43
Using Boolean algebra to simplify an equation
A + A.B
_
= A + B
Absorption
A+(A.B) + A.B
A+(B.A) + B.A
Commutative
A.B = B.A
Distributive
A + B.C = (A+B) . (A + C)
_
_
A+B(A + A)
_
A + A.B = A
19.3 Introduction to Boolean Algebra

## Slide 44
Using Boolean algebra to simplify an equation
A + A.B
_
= A + B
Absorption
A+(A.B) + A.B
A+(B.A) + B.A
Commutative
A.B = B.A
Distributive
A + B.C = (A+B) . (A + C)
_
_
A+B(A + A)
_
A + A.B = A
A+B(1)
A + A = 1
_
Inverse
A+B
19.3 Introduction to Boolean Algebra

## Slide 45
19.4 Practical Applications of Boolean Algebra
We can create a Boolean algebra expression with a truth table by applying the sum of products method. Eg. The Half Adder Truth Table.
C = A.B
Input | Input | Output | Output
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
S = A.B + A.B
_
_
Creating a Boolean algebra

## Slide 46
S = A.B + A.B
_
_
Creating a Boolean algebra (from a circuit)
Diagram
We will prove that:
Working
C
D
E
S = D.E
19.4 Practical Applications of Boolean Algebra

## Slide 47
S = A.B + A.B
_
_
Creating a Boolean algebra (from a circuit)
Diagram
We will prove that:
Working
C
D
E
C = A.B + A.B + A.B
_
Truth Table
INPUT
A
X
0
0
AND
B
0
1
1
0
1
1
X
0
0
0
1
NAND
1
1
1
0
_
_
_
19.4 Practical Applications of Boolean Algebra

## Slide 48
S = A.B + A.B
_
_
Creating a Boolean algebra (from a circuit)
Diagram
We will prove that:
Working
C
D
E
C = A.B + A.B + A.B
_
_
_
_
D = A . C
_
_
_
_
D = A . (A.B + A.B + A.B)
19.4 Practical Applications of Boolean Algebra

## Slide 49
S = A.B + A.B
_
_
Creating a Boolean algebra (from a circuit)
Diagram
We will prove that:
Working
C
D
E
D = A . C
_
_
_
_
D = A . (A.B + A.B + A.B)
Distributive
Law
D = A.A.B + A.A.B + A.A.B
_
_
_
_
A.(B+C) = A.B + A.C
19.4 Practical Applications of Boolean Algebra

## Slide 50
S = A.B + A.B
_
_
Creating a Boolean algebra (from a circuit)
Diagram
We will prove that:
Working
C
D
E
D = A . C
_
_
_
_
D = A . (A.B + A.B + A.B)
Distributive
Law
D = A.A.B + A.A.B + A.A.B
_
_
_
_
D = 0.B + A.A.B + 0.B
Inverse Law
_
_
A.A = 0
_
19.4 Practical Applications of Boolean Algebra

## Slide 51
S = A.B + A.B
_
_
Creating a Boolean algebra (from a circuit)
Diagram
We will prove that:
Working
C
D
E
D = A . C
_
_
_
_
D = A . (A.B + A.B + A.B)
Distributive
Law
D = A.A.B + A.A.B + A.A.B
_
_
_
_
D = 0.B + A.A.B + 0.B
Null Law
_
_
D = A.A.B
_
0.A = 0
Inverse Law
Idempotent
A.A = A
D = A.B
_
19.4 Practical Applications of Boolean Algebra

## Slide 52
S = A.B + A.B
_
_
Creating a Boolean algebra (from a circuit)
Diagram
We will prove that:
Working
C
D
E
D = A.B
_
De Morgan’s
A.B = A + B
D = A + B
_
_
_
Double Complement
A = A
_
_
D = A + B
_
19.4 Practical Applications of Boolean Algebra

## Slide 53
S = A.B + A.B
_
_
Creating a Boolean algebra (from a circuit)
Diagram
We will prove that:
Working
C
D
E
C = A.B + A.B + A.B
_
_
_
_
E = C . B
E = A + B
_
... after applying the same laws
19.4 Practical Applications of Boolean Algebra

## Slide 54
S = A.B + A.B
_
_
Creating a Boolean algebra (from a circuit)
Diagram
We will prove that:
Working
C
D
E
S = A + B . A + B
S = D.E
_
_
S = A.B + A.B
_
_
_
_
_
_
S = A.B + A.B
_
_
19.4 Practical Applications of Boolean Algebra

## Slide 55
19.5 Karnaugh maps (K-maps)
Previous solution - Sum of Product Method
Truth Table (Or Gate)
INPUT
A
X
0
0
OUTPUT
B
0
1
1
0
1
1
0
1
1
1
... after applying the same laws
A.B + A.B + A.B
_
_
A + B

## Slide 56
19.5 Karnaugh maps (K-maps)
 | 0 | 1
 | 1 | 1
What does a K-maps do?
Produce the simplest possible form for the Boolean algebra expression, and the process is much easier than the sum-of-products method.
Truth Table
INPUT
A
X
0
0
OUTPUT
B
0
1
1
0
1
1
0
1
1
1
A
A
B
B
_
_
K Map

## Slide 57
19.5 Karnaugh maps (K-maps)
 | 0 | 1
 | 1 | 1
What does a K-maps do?
How to find the expression from a KMAP?
A
A
B
B
_
_
K Map
  Identify groups (row, column, or square) of 1
  Group must contain 2,4, 8, etc cells
  Each group should be as large as possible
  Groups can overlap and all overlapping groups must be used
  If an individual cell cannot be contained in any group it is treated as being a group

## Slide 58
19.5 Karnaugh maps (K-maps)
 | 0 | 1
 | 1 | 1
What does a K-maps do?
Deriving the expression from a Kmap
A
A
B
B
_
_
K Map
A
Expression

## Slide 59
19.5 Karnaugh maps (K-maps)
 | 0 | 1
 | 1 | 1
What does a K-maps do?
Deriving the expression from a Kmap
A
A
B
B
_
_
K Map
A + B
Expression

## Slide 60
19.5 Karnaugh maps (K-maps)
What does a K-maps do?
Deriving the expression from a Kmap (Example 2)
 | 1 | 1
 | 1 | 0
Truth Table
INPUT
A
X
0
0
OUTPUT
B
0
1
1
0
1
1
1
1
1
0
A
A
B
B
_
_
K Map

## Slide 61
19.5 Karnaugh maps (K-maps)
What does a K-maps do?
Deriving the expression from a Kmap (Example 2)
 | 1 | 1
 | 1 | 0
A
A
B
B
_
_
K Map
A
Expression
_

## Slide 62
19.5 Karnaugh maps (K-maps)
What does a K-maps do?
Deriving the expression from a Kmap (Example 2)
 | 1 | 1
 | 1 | 0
A
A
B
B
_
_
K Map
A + B
Expression
_
_

## Slide 63
19.5 Karnaugh maps (K-maps)
What does a K-maps do?
Deriving the expression from a Kmap (Example 3, 3 inputs)
A
0
0
B
0
0
0
1
0
1
C
0
1
0
1
1
1
0
0
1
1
1
1
0
1
0
1
INPUT
OUTPUT
1
0
1
1
0
0
1
1
K Map
Truth Table
A
BC
0
1
00
01
11
10
Only 1 bit different
...
Gray coding sequence

## Slide 64
19.5 Karnaugh maps (K-maps)
What does a K-maps do?
Deriving the expression from a Kmap (Example 3, 3 inputs)
A
0
0
B
0
0
0
1
0
1
C
0
1
0
1
1
1
0
0
1
1
1
1
0
1
0
1
INPUT
OUTPUT
1
0
1
1
0
0
1
1
K Map
Truth Table
A
BC
0
1
00
01
11
10
1
0
0
0
1
1
1
1

## Slide 65
19.5 Karnaugh maps (K-maps)
What does a K-maps do?
Deriving the expression from a Kmap (Example 3, 3 inputs)
K Map
A
BC
0
1
00
01
11
10
1
0
0
0
1
1
1
1
B +
Expression

## Slide 66
19.5 Karnaugh maps (K-maps)
What does a K-maps do?
Deriving the expression from a Kmap (Example 3, 3 inputs)
K Map
A
BC
0
1
00
01
11
10
1
0
0
0
1
1
1
1
B + A.C
Expression

## Slide 67
19.5 Karnaugh maps (K-maps)
What does a K-maps do?
Deriving the expression from a Kmap (Example 4, 3 inputs)
A
0
0
B
0
0
0
1
0
1
C
0
1
0
1
1
1
0
0
1
1
1
1
0
1
0
1
INPUT
OUTPUT
0
0
1
1
1
1
1
1
K Map
Truth Table
A
BC
0
1
00
01
11
10
Only 1 bit different
Only 1 bit different
Only 1 bit different

## Slide 68
19.5 Karnaugh maps (K-maps)
What does a K-maps do?
Deriving the expression from a Kmap (Example 4, 3 inputs)
A
0
0
B
0
0
0
1
0
1
C
0
1
0
1
1
1
0
0
1
1
1
1
0
1
0
1
INPUT
OUTPUT
0
0
1
1
1
1
1
1
K Map
Truth Table
A
BC
0
1
00
01
11
10
Only 1 bit different
Only 1 bit different
Only 1 bit different
0
0
1
1
1
1
1
1

## Slide 69
19.5 Karnaugh maps (K-maps)
What does a K-maps do?
Deriving the expression from a Kmap (Example 4, 3 inputs)
K Map
A
BC
0
1
00
01
11
10
0
0
1
1
1
1
1
1
B
Expression

## Slide 70
19.5 Karnaugh maps (K-maps)
B + A
What does a K-maps do?
Deriving the expression from a Kmap (Example 4, 3 inputs)
K Map
A
BC
0
1
00
01
11
10
0
0
1
1
1
1
1
1
Expression