## Slide 1
Electricity and Circuits
Paper 2

## Slide 2
What is the structure of an atom?
Most of the mass is concentrated in the nucleus.
The electrons are arranged at different distances from the nucleus (different energy levels).
10.1 Structure of the Atom
Key Q

## Slide 3
Particle | Relative Charge
Proton | +1
Neutron | 0
Electron | -1
Why are atoms neutral?
Key Term | Definition
Atomic Number | The number of protons in an atom.
In an atom the number of electrons is equal to the number of protons in the nucleus.
This means that atom has no overall electrical charge.
All atoms of a particular element have the same number of protons.
10.1 Structure of the Atom
Key Q

## Slide 4
Component | Symbol | Component | Symbol
Open Switch |  | LED | 
Closed Switch |  | Lamp | 
Cell |  | Fuse | 
Battery |  | Voltmeter | 
Diode |  | Ammeter | 
Resistor |  | Thermistor | 
Variable Resistor |  | LDR | 
What are the different symbols for circuit components?
10.2 Electric Circuit Diagrams
Key Q

## Slide 5
What are series and parallel circuits?
Series Circuit
Parallel Circuit
10.3 Series and Parallel
Key Q

## Slide 6
What are series and parallel circuits?
Series Circuit
Parallel Circuit
There are two ways of joining electrical components, in series and in parallel.
Some circuits include both series and parallel parts.
10.3 Series and Parallel
Key Q

## Slide 7
What are the similarities and differences between series and parallel circuits?
In a series circuit..
The charge passes through all of the components so the current through each component is the same.
The potential difference is largest across the component with the greatest resistance.
The change in resistance of one component will cause a change in potential difference across all components
10.3 Series and Parallel
Key Q

## Slide 8
What are the similarities and differences between series and parallel circuits?
In a series circuit..
There is the same current through each component
The total potential difference of the power supply is shared between the components.
The total resistance of two components is the sum of the resistance of each component.
Rtotal = R1 + R2
10.3 Series and Parallel
Key Q

## Slide 9
What are the similarities and differences between series and parallel circuits?
In a parallel circuit..
Each charge passes through only one branch of the circuit.
The current is largest through the component with the smallest resistance.
10.3 Series and Parallel
Key Q

## Slide 10
What are the similarities and differences between series and parallel circuits?
In a parallel circuit..
The potential difference across each component is the same.
The total current through the whole circuit is the sum of the currents through the separate components
The total resistance of two resistors is less than the resistance of the smallest individual resistor.
10.3 Series and Parallel
Key Q

## Slide 11
How are ammeters and voltmeters connected within a circuit?
10.4 Voltmeter
Key Q

## Slide 12
How are ammeters and voltmeters connected within a circuit?
Voltmeters are connected in parallel across a component in a circuit
V
10.4 Voltmeter
Key Q

## Slide 13
What is potential difference?
10.5 Potential Difference
Key Q
Potential difference is the energy transferred per unit of charge that passes.
A volt is a joule per coulomb.

## Slide 14
Energy Transferred = Charge x Potential Difference
Joules
J
Coulombs
C
Volts
V
E = Q x V
You may need to convert units!
What is the equation that links charge moved, energy transferred and potential difference?
10.6 Energy Transferred
Key Q

## Slide 15
Convert Units | 50mA = 0.05
Write down the formula. | Q = I x t
Substitute Values | Q = 0.05 x 14,400
Do the Maths | Q = 720
Round and add units. | 720C
A torch worked for 14,400seconds before needing to be replaced. The current in the LED was 50mA. Calculate the charge flow. (3)
Usually 1 mark for this.
Show all of your working out.
10.9 Charge

## Slide 16
How are ammeters and voltmeters connected within a circuit?
10.7 Ammeter
Key Q

## Slide 17
How are ammeters and voltmeters connected within a circuit?
A
Ammeters are connected in series within a circuit
10.7 Ammeter
Key Q

## Slide 18
What is electric current?
Key Term | Definition
Electric Current | The flow of electrical charge.
10.8 Current
Key Q

## Slide 19
What is electric current?
An electric current is the rate of flow of charge in a circuit.
In an electric circuit the metal conductors (components and wires) contain many charges that are free to move.
When a circuit is made, the battery causes free charges to move.
These charges are not used up but flow in a continuous loop.
10.8 Current
Key Q

## Slide 20
What is electric current?
Charge Flow= Current x Time
Coulombs
C
Amperes
A
Seconds
s
Q = I x t
You may need to convert units!
Key Term | Definition
Electric Current | The flow of electrical charge.
10.9 Charge
Key Q

## Slide 21
Convert Units | 50mA = 0.05
Write down the formula. | Q = I x t
Substitute Values | Q = 0.05 x 14,400
Do the Maths | Q = 720
Round and add units. | 720C
A torch worked for 14,400seconds before needing to be replaced. The current in the LED was 50mA. Calculate the charge flow. (3)
Usually 1 mark for this.
Show all of your working out.
10.9 Charge

## Slide 22
Convert Units | 2mA = 0.02A
Write down the formula. | Q = I x t
Substitute Values | 8 = 0.02 x t
Do the Maths | t = 8 / 0.02 t = 400
Round and add units. | 400s
Calculate the time when charge flow is 8C and current is 2mA. (3)
Usually 1 mark for this.
Substitute before you do any rearranging. 1 mark for doing this.
Show each step that you do.
10.9 Charge

## Slide 23
When will there be a current in a circuit?
10.10 Closed Circuits
Key Q
This is a closed system.
There will be a current in a circuit if the system is closed…
..and there is a potential difference.

## Slide 24
What happens at a junction of a circuit?
10.11 Conservation of Current
Key Q
At the junction of a circuit current is conserved.

## Slide 25
What happens to current when resistance is increased?
10.12 Variable Resistors
Key Q
When resistance is high it is harder for electrons to move..
..this means that current will be lower.
When resistance is low it is easier for electrons to move..
..this means that current will be higher

## Slide 26
What happens to current when resistance is increased?
10.12 Variable Resistors
Key Q
A variable resistor can be used to change the resistance.

## Slide 27
What does current through a component depend on?
The current through a component depends on both the resistance of the component and the potential difference across it.
Potential Difference = Current x Resistance
Volts
V
Amperes
A
Ohms
Ω
V = I x R
You may need to convert units!
The greater the resistance of the component the smaller the current for a given potential difference.
10.13 Potential Difference
Key Q

## Slide 28
What does current through a component depend on?
In a given circuit, the larger the potential difference across the power supply the bigger the current.
Amperes
A
Ohms
Ω
Components such as resistors and lamps resist the flow of charge through them.
The resistance of connecting wires is usually so small that it can be ignored.
The larger the resistance in a given circuit, the smaller the current will be.
10.13 Potential Difference
Key Q

## Slide 29
Convert Units | 800mA = 0.8A
Write down the formula. | V = I x R
Substitute Values | V = 0.8 x 2.5
Do the Maths | V = 2
Round and add units. | 2V
A filament lamp has a current of 800mA through it and its resistance is 2.5Ω. Calculate the potential difference. (3)
Usually 1 mark for this.
Show all of your working out.
10.13 Potential Difference

## Slide 30
Convert Units | -
Write down the formula. | V = I x R
Substitute Values | 230 = 26 x R
Do the Maths | R = 230 / 26 R = 8.8461538462
Round and add units. | 8.8Ω
A hob draws a current of 26 A from the 230 V mains electricity supply. Calculate the resistance. (3)
Substitute before you do any rearranging. 1 mark for doing this.
Show each step that you do.
10.13 Potential Difference

## Slide 31
Which circuit has the higher resistance and why?
A
B
10.14 Resistance
Key Q

## Slide 32
Which circuit has the higher resistance and why?
A
B
B has the higher resistance.
This is because in a series circuit the current the resistance of components is combined
10.14 Resistance
Key Q

## Slide 33
Which circuit has the higher resistance and why?
B
A
10.14 Resistance
Key Q

## Slide 34
Which circuit has the higher resistance and why?
B
A
A has the higher resistance.
This is because in a parallel circuit the resistance drops when there are more paths for the current to flow.
10.14 Resistance
Key Q

## Slide 35
A | 0.36A
B | 0.12A
C | 0A
A1 has a reading of 0.36A. What is the current through A2?
10.15 Calculations in Circuits

## Slide 36
A | 230V
B | 0V
C | 115V
What is the potential difference if two lamps are connected in parallel?
10.15 Calculations in Circuits

## Slide 37
A | 230V
B | 0V
C | 115V
What is the potential difference if two lamps are connected in series?
10.15 Calculations in Circuits

## Slide 38
Brightness stays the same
Potential difference across each bulb in the same
10.15 Calculations in Circuits

## Slide 39
10.15 Calculations in Circuits

## Slide 40
I1 = I2 + I3
I2 = I3
I1 = 2I3
I1 = 2I2
10.15 Calculations in Circuits

## Slide 41
How can we determine the resistance of a component in a circuit?
Test
Component
Measure the current in the circuit using an ammeter.
Measure the voltage across the component.
10.16 and 17 Core Practical
Key Q

## Slide 42
How can we investigate the IV characteristics of a resistor?
1
Set up equipment as shown in the diagram.
10.16 and 17 Core Practical
Key Q

## Slide 43
How can we investigate the IV characteristics of a resistor?
1
Set up equipment as shown in the diagram.
2
Record the current and voltage.
3
Adjust the variable resistor 4 more times recording the new current and voltage each time.
4
Swap the leads on the battery so that the reading on the ammeter and voltmeter is negative.
5
Record the current and voltage 5 times adjusting the variable resistor between each reading.
10.16 and 17 Core Practical
Key Q

## Slide 44
How can we investigate the IV characteristics of a resistor?
6
Plot a graph of current against potential difference.
10.16 and 17 Core Practical
Key Q

## Slide 45
How can we investigate the IV characteristics of a filament lamp?
Set up equipment as shown in the diagram.
Notice it is the same as the earlier circuit with a filament lamp rather than a resistor.
Repeat using the same method that was used for the resistor.
10.16 and 17 Core Practical
Key Q

## Slide 46
How can we investigate the IV characteristics of a filament lamp?
Plot a graph of current against potential difference.
10.16 and 17 Core Practical
Key Q

## Slide 47
For some resistors, the value of R remains constant but that in others it can change as the current changes.
What is the relationship between current and potential difference for different components?
10.18 Current & Potential Difference
Key Q

## Slide 48
The current through an ohmic conductor (at a constant temperature) is directly proportional to the potential difference across the resistor.
This means that the resistance remains constant as the current changes.
What is the relationship between current and potential difference for ohmic resistors?
10.18 Current & Potential Difference
Key Q

## Slide 49
The resistance of a filament lamp increases as the temperature of the filament increases.
This means that the resistance is not constant as the current changes.
What is the relationship between current and potential difference for a filament lamp?
10.18 Current & Potential Difference
Key Q

## Slide 50
The current through a diode flows in one direction only. The diode has a very high resistance in the reverse direction.
What is the relationship between current and potential difference for a diode?
10.18 Current & Potential Difference
Key Q

## Slide 51
The resistance of an LDR decreases as light intensity increases.
In the dark and at low light levels, the resistance of an LDR is high and little current can flow through it.
In bright light, the resistance of an LDR is low and more current can flow through it
LDR’s are used in circuits to switch on lights when it gets dark.
What is an LDR and how does its resistance vary?
10.19 Light Dependent Resistors
Key Q

## Slide 52
The resistance of a thermistor decreases as the temperature increases.
At high temperatures, the resistance of a thermistor is low and more current can flow through them.
At high temperatures, the resistance of a thermistor is low and more current can flow through them.
Thermistors are used in thermostats.
What is a thermistor and how does its resistance vary?
10.20 Thermistors
Key Q

## Slide 53
How can we investigate the IV variation in resistance in components such as diodes?
Set up equipment as shown in the diagram.
Notice it is the same as the earlier circuit with a diode rather than a resistor or a filament lamp.
Repeat using the same method that was used for the resistor and filament lamp.
10.21 Design of Circuits
Key Q

## Slide 54
What happens to a resistor when a current passes through it?
10.22 Energy Transfers
Key Q
When a current passes through a resistor there is a transfer of energy.
This causes the resistor to warm up.

## Slide 55
What happens to the electrical energy when work is done in a circuit?
10.23 Dissipation of Electrical Energy
Key Q
Electrical energy is dissipated as thermal energy when an electric current does work against electrical resistance.
This is why filament light bulbs tend to get hot.
The filament has a high resistance and lots of energy is transferred to thermal energy.

## Slide 56
Why is energy dissipated in electric circuits when work is done?
10.24 Energy Transfers
Key Q
Energy is transferred to thermal energy because there are collisions between electrons and the ions in the metallic lattice.

## Slide 57
How can unwanted energy transfers be reduced in electrical circuits?
10.25 Reducing Energy Transfers
Key Q
Thicker wires could be used to reduce unwanted energy transfers.
Thicker wires have a lower resistance.
This means that less thermal energy is transferred in the wires.

## Slide 58
What are the advantages and disadvantages of the heating effect in circuits?
10.26 Heating Effect on Circuit
Key Q
Advantages | Disadvantages
Energy efficient way of transferring heat when used in heaters. | Energy can be wasted as heat
 | Warmth produced can damage the insulating wires
 | Pose a fire hazard
 | Can cause burns

## Slide 59
Energy Transferred = Power x Time
Joules
J
Watts
W
Seconds
s
E = P x t
You may need to convert units!
What does the amount of energy an appliance transfer depend on?
10.27 Energy Transferred
Key Q

## Slide 60
Convert Units | 1 minute = 60 seconds
Write down the formula. | E = P x t
Substitute Values | E = 800 x 60
Do the Maths | E = 48,000
Round and add units. | 48,000J
A toaster is on for 1 minute and has a power rating of 800W. Calculate the energy transferred (4)
Usually 1 mark for this.
Substitute before you do any rearranging. 1 mark for doing this.
Show each step that you do. 1 mark available here.
Answer to 2 s.f which is appropriate from values in the qu.
10.27 Energy Transferred

## Slide 61
Convert Units | 1.2kJ = 1200J
Write down the formula. | E = P x t
Substitute Values | 1200 = 900 x t
Do the Maths | t = 1200/900 t = 1.333333333
Round and add units. | 1.3s
A 900W microwave transfers 1.2kJ of energy. Calculate how long its turned on for.
Usually 1 mark for this.
Substitute before you do any rearranging. 1 mark for doing this.
Show each step that you do. 2 marks available here.
Answer to 2 s.f which is the same as the values in the qu.
10.27 Energy Transferred

## Slide 62
Task
 | Calculate energy transferred when time is 2 mins and power is 900W. | Calculate energy transferred when time is 30s and power is 1.8kW | Calculate power when 2.8kJ is transferred over 30 seconds.
Convert Units | 2mins = 120s | 1.8kW = 1800W | 2.8kJ = 2800J
Write down the formula. | E = P x t | E = P x t | E = P x t
Substitute Values | E = 900 x 120 | E = 1800 x 30 | 2800 = P x 30
Do the Maths | E = 108,000 | E = 54,000 | P = 2800 / 30 P = 93.33333333
Round and add units. | 108,000J | 54,000J | 93W
Complete the calculations for the following questions.
10.27 Energy Transferred

## Slide 63
What is power?
10.28 Energy Transferred
Key Q
Power is the energy transferred per second.
It is measured in watts.

## Slide 64
What does the amount of energy an appliance transfer depend on?
Power = Energy Transferred / Time
Watts
W
Joules
J
Seconds
s
P = E / t
You may need to convert units!
10.29 Power
Key Q

## Slide 65
Convert Units | 5 minutes = 300 seconds
Write down the formula. | P = E / t
Substitute Values | 750 = E / 300
Do the Maths | E = 750 x 300 = 225,000
Round and add units. | 225,000J
A microwave is on for 5 minutes and has a power rating of 750W. Calculate the energy transferred (4)
Usually 1 mark for this.
Substitute before you do any rearranging.
Show each step that you do.
10.29 Power

## Slide 66
Convert Units | 1.3kJ = 1300J
Write down the formula. | P = E / t
Substitute Values | 1200 = 1300 / t
Do the Maths | t = 1300/1200 t = 1.08333333333
Round and add units. | 1.1s
A 1200W microwave transfers 1.3kJ of energy. Calculate how long its turned on for.
Usually 1 mark for this.
Substitute before you do any rearranging.
Show each step that you do.
Answer to 2 s.f which is the same as the values in the qu.
10.29 Power

## Slide 67
What determines the power transfer in any circuit device?
10.30 Power
Key Q
The power transferred in a circuit device is determined by…
The potential difference across the circuit.
The current in the circuit

## Slide 68
How can we calculate power?
Power = Potential Difference x Current
Watts
W
Amperes
A
Potential Difference
V
P = V x I
OR
Power = (Current)2 x Resistance
Ohms
Ω
P = I2 x R
10.31 Electrical Power
Key Q

## Slide 69
What are domestic electrical appliances?
Key Term | Definition
Domestic Electrical Appliance | An object in the home that is designed to bring about energy transfers.
10.32 Domestic Devices
Key Q
The energy an appliance transfers depends on the power of the appliance and the time it is turned on for.

## Slide 70
What is the difference between direct and alternating voltage?
10.33 Direct and Alternating Voltage
Key Q
The voltage in direct voltage is always constant.
This can be either positive or negative.
The current in the circuit will also be direct.

## Slide 71
What is the difference between direct and alternating voltage?
10.33 Direct and Alternating Voltage
Key Q
The voltage in alternating voltage is constantly changing.
The voltage will periodically change from positive to negative and visa versa
The current in the circuit will also be alternating

## Slide 72
What is direct and alternating current?
Key Term | Definition | Example of Source
Direct Current | A current that passes in the same direction | Current produced by cells and batteries.
Alternating Current | A current that changes direction. | Current in the national grid.
10.34 Direct Current
Key Q

## Slide 73
What is alternating current?
10.35 Alternating Current
Key Q
An electric current that regularly changes its direction and size.
On a voltage-time graph, this would appear as a curve alternating between positive and negative voltages.
The positive and negative values indicate the direction of current flow.

## Slide 74
What is the potential difference and frequency of electricity in the UK?
Mains electricity in the UK is an ac supply.
It has a frequency of 50Hz.
Potential difference is 230V
10.36 UK Domestic Supply
Key Q

## Slide 75
How does a plug work?
Most electrical appliances are connected to the mains using three-core cable.
The insulation covering each wire is colour coded for easy identification.
10.37 Live and Neutral Wires
Key Q

## Slide 76
How does a plug work?
Wire | Colour | Description | Potential Difference
Live Wire | Brown | Carries the alternating potential difference from the supply. | 230V
Neutral Wire | Blue | Completes the circuit. | 0V (or close to)
Earth Wire | Green and Yellow Stripes | Safety wire to stop the appliance becoming live. | 0V
10.37 Live and Neutral Wires
Key Q

## Slide 77
How does a plug work?
Wire | Colour | Description | Potential Difference
Live Wire | Brown | Carries the alternating potential difference from the supply. | 230V
Neutral Wire | Blue | Completes the circuit. | 0V (or close to)
Earth Wire | Green and Yellow Stripes | Safety wire to stop the appliance becoming live. | 0V
10.38 Earth Wire
Key Q

## Slide 78
What happens if the current in a circuit is too high?
If the current in a circuit were to be too high the fuse in the plug should melt.
This will break the circuit and will stop the flow of current and protects the appliance if something goes wrong.
10.39 Switches and Fuses
Key Q

## Slide 79
How does a plug work?
Wire | Colour | Description | Potential Difference
Live Wire | Brown | Carries the alternating potential difference from the supply. | 230V
Neutral Wire | Blue | Completes the circuit. | 0V (or close to)
Earth Wire | Green and Yellow Stripes | Safety wire to stop the appliance becoming live. | 0V
10.40 Potential Difference in Wires
Key Q

## Slide 80
Why a live wire may be dangerous even when a switch is open?
A live wire may be dangerous even when a switch is open.
This is because if the circuit were to be accidently complete then there would be a large potential difference.
This large potential difference could then cause electrocution.
10.41 Dangers of Live Wire
Key Q

## Slide 81
Why it is dangerous if a live wire and earth wire are connected?
A live wire and earth wire should not be connected together.
This is because if they were to touch there would be a complete circuit from the live circuit to the ground. T
This can cause shocks or fires.
10.41 Dangers of Live Wire
Key Q

## Slide 82
What are domestic electrical appliances?
An object in the home that is designed to bring about energy transfers.
10.42 Power Ratings
Key Q

## Slide 83
What does the amount of energy an appliance transfer depend on?
The energy an appliance transfers depends on the power of the appliance and the time it is turned on for.
10.42 Power Ratings
Key Q

## Slide 84
What is the relationship between power ratings for domestic electrical appliances and the changes in stored energy?
10.42 Power Ratings
Key Q
All electrical appliances transfer energy from one store to another.
The higher the power rating of an appliance the greater the transfer of energy in a fixed period of time.
1000W