## Slide 1: Units

## Slide 2: Learning objectives
Calculate the range of values for a given number of bits
Explain that multiple bytes can be referred to using binary prefixes
Convert between different units

## Slide 3: Bits, Nibbles and Bytes
A bit is the fundamental unit of binary numbers. A bit is a binary digit that can be either 0 or 1.
Bit is short for binary digit
A byte contains 8 bits
A nibble contains 4 bits
In abbreviation we use lower-case b for bits and upper-case B for Bytes

## Slide 4: Bits, Nibbles and Bytes
The number of different values that can be represented by a sequence of bits is 2n where n is the number of bits.
If we have 2 bits we have four combinations (values): 00,01,10,11
A sequence of 3 bits can give us 23 (2x2x2) values which is 8: 000,001,010,011,100,101,110,111
How many different values do we have for 4 bits, and what are the values?
The 16 combinations with 4 bits
0 0 0 0
0 0 0 1
0 0 1 0
0 0 1 1
0 1 0 0
0 1 0 1
0 1 1 0
0 1 1 1
1 0 0 0
1 0 0 1
1 0 1 0
1 0 1 1
1 1 0 0
1 1 0 1
1 1 1 0
1 1 1 1

## Slide 5: Complete the following table
Number of bits | How many different numbers
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
Number of bits | How many different numbers
1 | 2
2 | 4
3 | 8
4 | 16
5 | 32
6 | 64
7 | 128
8 | 256

## Slide 6: Bits and maximum value
Given a number of bits the maximum number can be calculated by converting all the digits to 1 and converting back to denary.
For instance, if we wish to calculate the maximum value for a number of 3 bits, we write down 111 and the convert to denary which is 1+2+4=7
The other way of calculating this is to use the formula:
2n-1 where n is the number of bits.
So if we have 3 bits then we have 23-1 = 2 x 2 x 2 -1 = 7
https://youtu.be/Mkr8M-Y2zIE

## Slide 7: What is the maximum value if you have the following number of bits?
2 bits
3 bits
1 byte
1 nibble
4 bits
8 bits
9 bits
10 bits
2 bytes
3
7
255
15
15
255
511
1023
65535

## Slide 8: Misconception
For a given number of bits:
The maximum number is: 2n-1. For instance, if we have 3 bits the maximum value is: 23-1 = 7
The number of numbers is 2n. For unsigned integers the minimum and maximum values are 0 and 2n-1 respectively where n is the number of bits.
Do not get confused between the maximum value (2n-1) and number of values (2n) that can be represented for a given number of bits

## Slide 9: Complete the following table
Number of bits, n | Max integer 2n-1 | Number of different integers 2n
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
8 |  | 
Number of bits, n | Max integer 2n-1 | Number of different integers 2n
1 | 1 | 2
2 | 3 | 4
3 | 7 | 8
4 | 15 | 16
5 | 31 | 32
6 | 63 | 64
7 | 127 | 128
8 | 255 | 256

## Slide 10: Given a decimal number what is the minimum number of bits needed to represent that value?
Worked example: What is the minimum number of bits needed to represent the decimal number 21
Convert to binary 21 in binary is: 00010101
Count up number of bits ignoring preceding 0s. This is 5
https://youtu.be/3q8Y0ExwhRU

## Slide 11: What is the minimum number of bits needed to represent the following numbers?
17
255
123
91
1053
10271
5
8
7
7
11
14

## Slide 12: Units: Powers of 10
Unit | Symbol | Number of bytes
Kilobyte | KB | 103 (1000)
Megabyte | MB | 106 (1 million)
Gigabyte | GB | 109 (1 billion)
Terabyte | TB | 1012 (1 trillion)
Petabyte | PB | 1015
Exabyte | EB | 1018
Zettabyte | ZB | 1021
Yottabyte | YB | 1024
Googolplex |  | 10^(10^100)
Zoogolplex |  | 10^(10^1000000)

## Slide 13: Approximately what size are the following
 | Approximate size
A photo taken on a mobile phone | 
A MP3 song file | 
Typical UK broadband speed | 
Capacity of floppy disk | 
Size of a LD film | 
Size of a HD film | 
Capacity of a DVD | 
Capacity of a Blu Ray | 
Word/Pdf document | 
Image download from the web | 
Phone dial up with modem | 
Size of hard disk in the 1990s | 
Size of hard disk in 2021 | 
How much data is being uploaded to Facebook each minute | 

## Slide 14: Approximately what size are the following
 | Approximate size
A photo taken on a mobile phone | 10-20 MB
A MP3 song file | 3-4 MB
Typical UK broadband speed | 15-50Mbits/s(Mb/s)
Capacity of floppy disk | 1.4MB
Size of a LD film | 4-7GB
Size of a HD film | 20-25GB
Capacity of a DVD | 4-7GB
Capacity of a Blu Ray | 25GB
Word/Pdf document | 26 Kilobytes + 4 Kilobytes per page
Image download from the web | 1kB to 5MB
Phone dial up with modem | 56 Kilobits per second
Size of hard disk in the 1990s | 10 GB
Size of hard disk in 2021 | 1TB
How much data is being uploaded to Facebook each minute | 3 Terrabytes per minute

## Slide 15: Converting between units: Worked example
What is 4000 bits in Kilobytes?
Convert to bytes: 4000 bits = 4000 / 8 = 500B
Convert from bytes to kilobytes: 500 = 500 / 1000 = 0.5KB

## Slide 16: Unit Conversions: Complete the following table
Bits | Bytes | KB | MB | GB
800,000,000 |  |  |  | 
 |  | 4000 |  | 

## Slide 17: Unit Conversions: Complete the following table
Bits | Bytes | KB | MB | GB
800,000,000 | 100,000,000 | 100,000 | 100 | 0.1
32,000,000 | 4,000,000 | 4000 | 4 | 0.004

## Slide 18: Worked example: Comparing units
Which is bigger 6000 bits or 4KB?
When comparing between units convert all units into a common unit. We will convert both units into Bytes.
6000 bits / 8 = 750 Bytes
4KB x 1000 = 4000 Bytes
Therefore, 4KB is greater than 6000 bits
https://youtu.be/bOaY04BzX_Y

## Slide 19: Which is bigger?
4000 bits or 600 Bytes
8000 bits or 1KB
1000KB or 800000 bits
10KB or 0.1MB
400MB or 1GB
600 Bytes
Same
1000KB
0.1MB
1GB

## Slide 20: Units: Put the following in the correct order from largest to smallest
8000 bits | 
800 bytes | 
2 kiloBytes | 
1 megaByte | 
1 gigabyte | 
3 billion bytes | 
8 billion bits | 
2000 megabytes | 
2 terrabytes | 
1000 gigabytes | 

## Slide 21: Units: Put the following in the correct order from largest to smallest
8000 bits 1000 bytes | 3
800 bytes | 4
2 KBytes 2000 bytes | 2
1 megabyte 1,000,000 bytes | 1
1 gigabyte 1 billion bytes | 3
3 billion bytes | 1
8 billion bits 1 billion bytes | 3
2000 megabytes 2 billion bytes | 2
2 terrabytes | 1
1000 gigabytes 1 terra byte | 2

## Slide 22: Power of 2 Units
Unit | Symbol | Number of bytes
Kilobyte | kB | 103 (1000)
Megabyte | MB | 106 (1 million)
Gigabyte | GB | 109 (1 billion)
Terabyte | TB | 1012 (1 trillion)
Unit | Symbol | Number of bytes
KibiByte | KiB | 210 (1024)
MebiByte | MiB | 220 (1,048,576)
GibiByte | GiB | 230
TebiByte | TiB | 240
Power of 2
Power of 10

## Slide 23: Units
We often state that a kilobyte is 1024 bytes but this is not strictly true because a kilobyte is 1000 bytes.
Strictly speaking 1024 (210) Bytes is not a KiloByte.
1024 Bytes is called a KibiByte.
Lots of people refer to 1024 Bytes as a KiloByte partly because it makes calculations easier when they only require an estimate. After all multiplying and dividing by 1000 is much easier than multiplying and dividing by 1024.

## Slide 24: Units
Powers of 2 units including kibibytes, mebibytes, gibibytes and tebibytes were introduced to allow us to refer to the number of bytes unambiguously.
We should therefore use kibibytes to refer to 1024 bytes. This also applies elsewhere where we often use megabytes, gigabytes and terrabytes when we should use mebibytes, gibibytes and tebibytes, respectively.
There is only a small difference in the number of bytes between kB and KiB, but this increases significantly for larger powers such as between yottabytes (1024) and yobibytes (280).

## Slide 25: Units: Put the following in the correct order from largest to smallest
1 mebibyte | 
8000 bits | 
800 bytes | 
2 kilobyte | 
1 kibibyte | 
1 megabyte | 
1000 mebibytes | 
1 gigabyte | 
1 gibibyte | 
3 billion bytes | 
8 billion bits | 
2000 megabytes | 
1 tebibyte | 
2 terrabytes | 
1000 gigabytes | 
3000 gibibytes | 

## Slide 26: Units: Put the following in the correct order from largest to smallest
1 mebibyte 1048576 bytes | 1
8000 bits 1000 bytes | 5
800 bytes | 6
2 kilobyte 2000 bytes | 3
1 kibibyte 1024 bytes | 4
1 megabyte 1,000,000 bytes | 2
1000 mebibytes 1,048,576,000 | 4
1 gigabyte 1,000,000,000 | 5=
1 gibibyte 1,073,741,824 | 3
3 billion bytes 3,000,000,000 | 1
8 billion bits 1,000,000,000 | 5=
2000 megabytes 2,000,000,000 | 2
1 tebibyte 1,099,511,627,776 | 3
2 terrabytes 2,000,000,000,000 | 2
1000 gigabytes 1,000,000,000,000 | 4
3000 gibibytes 3,221,225,472,000 | 1

## Slide 27: Plenary:
If you have a 1 GB SD memory storage device on your camera, how many 30MB photographs could you store?
If you have 1TB storage on your computer how many 10MB songs can you store? (Ignore space take up by software applications)
I have a file of 1500 KB that I wish to send as an attachment by email, however the maximum size of file that I am allowed to send is 8MB. Can I send the file?
I have an internet speed of 56 kilobits (Kbs) per second and I wish to download a 3 Megabyte MP3 song. Assuming there are no other demands on the internet connection, approximately how long will it take for me to download the file in minutes?
In the late 1990s a typical hard disk in a standard PC was approximately 10 GBytes. In 2021 a typical hard disk is 1 TerraByte. Approximately how many times more storage capacity is available today than 20 years ago.
Answers:
1000/30=33
1,000,000,000,000 /10,000,000 = 100,000
1.5MB < 8MB: Yes
56/8=7000Bytes 3000/7 / 60 = 7 minutes
1,000,000,000,000 / 10,000,000,000 = 100

## Slide 28: Homework
Practicing listing all powers of 2 and powers of 10 units in order by size from memory
Unit | Symbol | Number of bytes
Kilobyte | kB | 103 (1000)
KibiByte | KiB | 210 (1024)
Megabyte | MB | 106 (1 million)
MebiByte | MiB | 220 (1,048,576)
Gigabyte | GB | 109 (1 billion)
GibiByte | GiB | 230
Terabyte | TB | 1012 (1 trillion)
TebiByte | TiB | 240